## Slide 1
There are many applications that require a dedicated timer system, including:
    Delay creation and measurement
    Period and Pulse-width measurement
    Frequency measurement
    Event counting
    Arrival time comparison
    Time-of-day tracking
    Waveform generation
    Periodic interrupt generation
Timer Functions

## Slide 2
Without a dedicated timer system, some of these applications would be very difficult to implement.
The HCS12 includes a powerful timer system to support these applications.
At the heart of the HCS12 timer system is the 16-bit timer-counter (TCNT). This counter can be read at any start or stop of an event, as you like.
One of the timer/counter functions is called input-capture. This function copies the content of the 16-bit timer to a latch when the specified event arrives.
By capturing the timer value, many measurements can be made. Such as:
Timer Functions cont’d …
Pulse-width measure. | Period measurement | Duty cycle measure.
Event arrival time rec. | Time reference | 

## Slide 3
Another function of timer is called the output-compare. The output-compare circuit compares the 16-bit timer value with that of the output-compare register in each clock cycle and performs one or combination of the following events:
    Trigger an action in a pin
    Set a flag in register
    Generate an interrupt request
The key to using the output-compare function is to make a copy of the 16-bit timer, add a delay to it, and store the sum in an output-compare register.
The HCS12 has 8 output-compare channels, which share the signal pins and registers with input-capture channels.
The third timer function is pulse accumulator. This circuit is often used to count the events arriving in a certain interval or measure the frequency of the unknown signal.
Timer Functions cont’d …

## Slide 4
Certain HCS12 members (for example, A family, C family, and H family) implement a Standard Timer Module (TIM) that consist of eight channels of input-capture/output-compare functions and a 16-bit pulse accumulator, PACA.
Other HCS members add additional features to the TIM module, and the resultant module is referred to as Enhanced Capture Timer Module (ECT).
The design goal of the ECT is to support the requirements of automotive, process control, and other applications that need additional timer features.
The timer/counter module shares Port T (PT7 ~ PT0) which correspond to IOC7 ~ IOC0.
The 16-bit pulse accumulator shares the use of the PT7 pin which is referred to as the PAI pin in this case.
Timer Functions cont’d …

## Slide 5
Timer Functions cont’d …
Input Capture
Output Compare
Channel 0
Input Capture
Output Compare
Channel 1
Input Capture
Output Compare
Channel 2
Input Capture
Output Compare
Channel 3
Input Capture
Output Compare
Channel 4
Input Capture
Output Compare
Channel 5
Input Capture
Output Compare
Channel 6
Input Capture
Output Compare
Channel 7
IOC0
IOC1
IOC2
IOC3
IOC4
IOC5
IOC6
IOC7
Prescaler
Bus clock
16-bit pulse accumulator A
Registers
16-bit counter
Timer overflow interrupt
TC0 interrupt
TC1 interrupt
TC2 interrupt
TC3 interrupt
TC4 interrupt
TC5 interrupt
TC6 interrupt
TC7 interrupt
PA overflow interrupt
PA input interrupt
HCS12 Standard Timer (TIM) Block Diagram

## Slide 6
Timer Counter Registers
There are three registers related to the operation of the TCNT counter. They are
  Timer System Control Register 1 (TSCR)
  Timer System Control Register 2 (TMSK2)
  Timer Interrupt Flag 2 Register (TFLG2)
Timer System Control Register 1
The timer counter must be enabled before it can count.
Setting bit 7 of the TSCR register enables the TCNT to count up.
The timer function can be stopped by setting the bit 6 of TSCR during the wait mode to save more power.

## Slide 7
TEN
TSWAI
TSfRZ
TffCA
0
0
0
0
0
0
0
0
0
0
0
0
Timer System Control Register 1 (TSCR)
  TEN – timer enable bit
  0 = disable timer; this can be used to save power consumption.
  1 = allows timer to function normally.
  TSWAI – timer stops while in wait mode bit.
  0 = allow timer to continue running during wait mode.
  1 = disable timer when MCU is in wait mode.
  TSFRZ – timer and modulus counter stop while in freeze mode.
  0 = allows timer and modulus counter to continue running during freeze mode.
  1 = disable timer and modulus counter when MCU is in freeze mode.
  TFFCA – timer fast flag clear all bit
  0 = allows timer flag clearing to function normally.
  1 = for TFLG1, a read from an input capture or a write to the output compare
  channel causes the corresponding channel flag, Cnf, to be cleared. For TFLG2,
  any access to the TCNT register clears the TOF flag. Any access to PACN3
  and PACN2 registers clears the PAOVF and PAIF flags in the PAFLG
  register. Any access to PACN1and PACN0 registers clear the PBOVF flag in
  the PBFLG register.
Timer Counter Registers cont’d …
All timer interrupt flags can be cleared by writing a 1 to them.
There is a faster way to clear timer flags. When bit 4 of the TSCR register is set to 1, a read from or a write to the appropriate TC register will clear the corresponding flag.

## Slide 8
Timer Counter Registers cont’d …
Timer System Control Register 2 (TMSK2)
The clock rate of the timer counter is set through this control register.
The clock rate can be pre-scaled through prescale bits of TMSK2, if bits 2 and 3 of PACTL register are set to 00.
TOI
0
0
0
TCRE
PR2
PR1
PR0
0
0
0
0
0
0
0
0
Timer System Control Register 2 (TMSK2)
  TOI – timer overflow interrupt enable bit
  0 = interrupt inhibited.
  1 = interrupt requested when TOF flag is set.
  TCRE – timer counter reset enable bit.
  0 = counter reset inhibited and counter free runs.
  1 = counter resets by a successful output compare 7.
  If TC7 = $0000 and TCRE = 1, TCNT stays at
  $0000 continuously.
  If TC7 = $FFFF and TCRE = 1, TOF will never
  be set when TCNT rolls over from $FFFF to
  $0000.
PR2 PR1 PR0 | Prescale Factor
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 2 4 8 16 32 64 128

## Slide 9
Timer Counter Registers cont’d …
TMSK2 [$004D]
TFLG2 [$004F]
TCNT [$0044-45]
Interrupt [$FFDE-DF]
16-bit Free Running Counter
Holding Register
Flag 2 Reg.
M
V
Pr
M
U
X
E Clock
÷1
÷2
÷2
÷2
÷2
÷2
÷2
÷2
TSCR [$0046]
0 0 0 0
0 0 0
0
Bit 7
Bit 7

## Slide 10
Timer Counter Registers cont’d …
Example:
Write a program to blink LEDs every time that timer overflows. Be aware of the speed of overflow! To accomplish this you need to do the followings:
    Enable timer/counter module and set quick erase.
    Set the speed of the timer/counter.
    Enable the appropriate interrupt for this purpose and clear flag.
    Enable the global interrupt.
    Write your interrupt handler to turn the LEDs ON or OFF alternatively. Make sure while you are in the handler to clear the interrupt flag.
    Put the interrupt handler’s starting address at appropriate place.
    Main program should stay in an infinite loop.
    Assemble, download, and run your program.

## Slide 11
#include reg9s12.h
ORG $1000
MOVW #tov_is,$3E5E ; set TCNT overflow interrupt vector
MOVB #$90,TSCR ; enable timer/counter & fast clear
MOVB #$87,TMSK2 ; set pre-scale factor to 128 and enable
; overflow interrupt
BSET DDRB,$FF ; make port B output port
BSET DDRP,$FF ; make port P output port
BSET DDRJ,$02 ; make bit 1 of port J output
BSET PTP,$FF ; disable 7-segment LEDs
BCLR PTJ,$02 ; enable LEDs
MOVB #$80,TFLG2 ; clear overflow flag
CLI ; enable global interrupt
forever JMP forever ; infinite loop
tov_is LDD TCNT ; clear TOF flag
COM PORTB ; complement port B
LDD #'.' ; ASCII value of period in D
LDX putchar ; output period to terminal
JSR 0,X ;
RTI
putchar EQU $EE86
END
Timer Counter Registers cont’d …

## Slide 12
Input-Capture Function
Some applications need to know the arrival time of events. In a computer, physical time is represented by the count in a counter.
The occurrence of an event is represented by a signal edge (either the rising or falling edge). The time when an event occurs can be recorded by latching the count value when a signal edge arrives.
Rising edge
Falling edge
or
The HCS12 timer system has eight input-capture channels that implement this operation.

## Slide 13
Input-Capture Function cont’d …
Each input-capture channel includes a 16-bit input-capture register, an input pin, input edge detection logic, and an interrupt generation circuit.
In the HCS12, physical time is represented by the count in the timer counter (TCNT).
Input-Capture/Output-Compare Selection
Since input-capture and output-compare functions share signal pins and registers, they cannot be enabled simultaneously.
The selection is done by the Timer Input-capture/Output-compare Select Register (TIOS).
IOS7
IOS6
IOS5
IOS4
IOS3
IOS2
IOS1
IOS0
0
0
0
0
0
0
0
0
Timer Input-capture/Output-compare Select register (TIOS)
  IOS[7:0] – input-capture or output-compare channel configuration bit
  0 = the corresponding channel acts as an input-capture.
  1 = the corresponding channel acts as an output-compare.

## Slide 14
Input-Capture Function cont’d …
Pins for Input-Capture
Port T has eight signal pins (PT7 ~ PT0) that can be used as input-capture/output-compare or general purpose I/O pins.
Pins PT3 ~ PT0 can also be used as the pulse accumulator input (PA3 ~ PA0).
The user must make sure that the PT3 ~ PT0 pins are enabled for one and only one of these three functions (OCn, ICn, or PAn).
When these pins are not used for timer functions, they can also be used as general-purpose I/O pins.
In this case, the user must use the DDRT register to configure the pin direction (input or output).
When a port T pin is used as a general-purpose I/O pin, its value is reflected in the corresponding bit in the PTT register.

## Slide 15
Input-Capture Function cont’d …
Registers Associated with Input-Capture
The user needs to specify what signal edge to capture. The edge selection is done via the Timer Control Registers 3 and 4.
EDG7B
EDG7A
EDG6B
EDG6A
EDG5B
EDG5A
EDG4B
EDG4A
0
0
0
0
0
0
0
0
Timer Control register 3 (TCTL3)
EDG3B
EDG3A
EDG2B
EDG2A
EDG1B
EDG1A
EDG0B
EDG0A
0
0
0
0
0
0
0
0
Timer Control register 4 (TCTL4)
  EDGnB EDGnA – edge configuration (n = 0 … 7)
  0 0 : capture disabled
  0 1 : capture on rising edge only
  1 0 : capture on falling edge only
  1 1 : capture on both edges

## Slide 16
Input-Capture Function cont’d …
When an input-capture channel is selected but capture is disabled, the associated pin can be used as a general-purpose I/O pin.
An interrupt-capture channel can optionally generate an interrupt request on the arrival of the selected edge if it is enabled.
The enabling of interrupt is controlled by the Timer Interrupt Enable register (TMSK1).
When a selected edge arrives at the input-capture pin, the corresponding flag in the Timer Flag register 1 (TFLG1) will be set.
C7I
C6I
C5I
C4I
C3I
C2I
C1I
C0I
0
0
0
0
0
0
0
0
Timer Interrupt Enable register (TMSK1)
  C7I – C0I : input-capture/output-compare interrupt enable bit
  0 = interrupt disabled.
  1 = interrupt enabled.

## Slide 17
C7F
C6F
C5F
C4F
C3F
C2F
C1F
C0F
0
0
0
0
0
0
0
0
Timer Interrupt Flag 1 register (TFLG1)
  C7F – C0F : input-capture/output-compare interrupt flag bits
  0 = interrupt condition has not occurred.
  1 = interrupt condition has occurred.
Input-Capture Function cont’d …
To clear a flag in TFLG1 register, write a 1 to it. However, there is a better way to clear the flag that incurs less overhead.
Setting bit 4 (TFFCA) of the TSCR register allows one to clear a flag by reading the corresponding input-capture register or writing a new value into the output-compare register.
Clearing the flag is needed for both operation of input-capture/output-compare functions.
Each input-capture channel has a 16-bit register (TCx, x = 0 to 7) to hold the count value when the selected signal edge arrives at the pin.

## Slide 18
Input-Capture Function cont’d …
PT0
Rise edge
Fall edge
Free Running Counter
Input-Capture 0 Register
bit 0
Interrupt
[$FFEE – EF]
TC0
[$0050 – 51]
TFLG1
[$004E]
TMSK2
[$004C]
TCTL4
[$004B]
bit 1
bit 0
Input Capture Channel 0
bit 0
TCNT
[$0044 – 45]

## Slide 19
Input-Capture Applications
Event arrival-time recording:
Sometimes an application needs to compare the arrival of several different events such as swimming competition.
The number of events that can be compared is limited by the number of input-capture channels.
Period measurement :
To measure the period of an unknown signal, the input-capture function should be configured to capture the main timer values corresponding to two consecutive rising or falling edges.
Period
Period

## Slide 20
Pulse width
Input-Capture Applications cont’d …
Pulse width measurement:
To measure the width of a pulse, the rising and falling edges are captured.
Since the free-running timer is 16 bit wide, it can only measure a signal period (or pulse width) no longer than 216 E clock cycles.
If the period of a slower signal is to be measured, the number of timer overflows that occur between the two edges must be taken into account.
Interrupt generation :
All input-capture pins can serve as edge-sensitive interrupt sources. Once enabled, interrupts will be generated on the selected edge(s).
Event Counting :
An event can be represented by a signal edge. An input-capture channel can be used in combination with an output-compare function to count the number of events that occur during an interval .
Whenever an edge arrives, an interrupt is generated. An event counter can be setup and incremented by the input-capture service routine.

## Slide 21
Start of
interval
End of
interval
e1
e2
e3
e4
ei
...
...
Input-Capture Applications cont’d …
ej
Time reference :
In this application, an input-capture function is used in conjunction with an output-compare function.
For example if the user wishes to activate an output signal a certain number of clock cycles after detecting an input event (a rising or falling edge ), the input-capture function will be used to record the time at which the edge is detected.
A number corresponding to the desired delay would be added to this captured value and stored in an output compare register.
Time t0
Time t0 + delay
Time of reference
(set up by signal edge
Time to activate
the output signal
(set up by output-compare

## Slide 22
Input-Capture Applications cont’d …
Duty cycle measurement :
The duty cycle is the percent of time that the signal is high within a period in a periodic digital signal.
The duty cycle can be measured as follow:
Phase difference measurement :
The phase difference is defined as the difference of arrival times (in percentage of period) of two signals that have the same frequency but do not coincide on their rising and falling edges.
The phase difference can be measured as follow:
Signal S2
Signal S1

## Slide 23: Sequence of Operation of the Input-Capture Subsystem
When an edge is detected by the input-capture pin, the value of the timer counter register is latched into the corresponding input-capture register.
As soon as the value of the timer counter register is latched, the corresponding flag in the Flag 1 register is immediately set to 1.
If the corresponding input-capture interrupt enable bit in the TMSK1 register is set, the detected edge also generates an interrupt.

## Slide 24: Input-Capture Interrupt Vectors
Channel | Pin | Vector Address | RAM Vector Address | Bit of TIE | Bit of TFLG1 | Edge-selection bits | Address of IC Register
IC0 IC1 IC2 IC3 IC4 IC5 IC6 IC7 | PT0 PT1 PT2 PT3 PT4 PT5 PT6 PT7 | $FFEE – EF $FFEC – ED $FFEA – EB $FFE8 – E9 $FFE6 – E7 $FFE4 – E5 $FFE2 – E3 $FFE0 – E1 | $3E6E $3E6C $3E6A $3E68 $3E66 $3E64 $3E62 $3E60 | 0 1 2 3 4 5 6 7 | 0 1 2 3 4 5 6 7 | TCTL4(1:0) TCTL4(3:2) TCTL4(5:4) TCTL4(7:6) TCTL3(1:0) TCTL3(3:2) TCTL3(5:4) TCTL3(7:6) | $0050 – 51 $0052 – 53 $0054 – 55 $0056 – 57 $0058 – 59 $005A – 5B $005C – 5D $005E – 5F

## Slide 25
Input-Capture Applications cont’d …
Example-1 of period measurement :
Use the input-capture channel 0 to measure the period of an unknown signal. The period is known to be shorter than 128 ms. Assume that E clock frequency is 24 MHz. Use the number of clock cycles as the unit of the period.
Solution :
Since the input-capture register is 16-bit, the longest period of the signal that can be measured with the prescaler to TCNT set to 1 is: 216 ÷ 24 MHz = 2.73 ms.
To measure a period that is equal to 128 ms, we have two options:
  Set the prescale factor to 1 and keep track of the number of times that the timer counter overflows.
  Set the prescale factor to 64 and do not keep track of the number of times that the timer counter overflows.
In this example, we will adopt the second approach to make the programming easier. The result of this measurement will be in number of clock cycles, and the period of each clock cycle is 2.67 s.

## Slide 26
one Period
HCS12
PT0
Input-Capture Applications cont’d …
Start
yes
Choose to capture the rising edge
Set the timer prescale to 16.
Enable the timer counter.
Clear C0F flag
C0F = 1?
Save the captured 1st edge
Clear the C0F flag
C0F = 1?
Take the difference of 1st & 2nd captured edges.
Stop
yes
no
no
Logic flow of the period-
measurement program.

## Slide 27
Input-Capture Applications cont’d …
*************************************************************************************************
* Measuring period up to 128 ms width using Input-capture *
*************************************************************************************************
#include reg9s12.h
ORG $1000
MOVB #$90,TSCR ; enable timer/counter & fast clear
BCLR TIOS,$01 ; enable input-capture 0
MOVB #$06,TMSK2 ; disable TCNT overflow interrupt,
* ; set prescaler to 64
MOVB #$01,TCTL4 ; capture the rising edge of PT0 signal
MOVB #$01,TFLG1 ; clear the C0F flag
wait BRCLR TFLG1,$01,wait ; wait for the arrival of 1st rising edge
MOVW TC0,period ; save the 1st edge & clear flag C0F
wait1 BRCLR TFLG1,$01,wait1 ; wait for the arrival of 1st rising edge
LDD TC0 ; grab the 2nd edge
CPD period ; which edge is larger
BLO comp
SUBD period ; subtract 1st from 2nd number
JMP res
comp COM period ; complement 1st number
COM period+1 ; and add to 2nd number
ADDD period
res STD period ; save the result
SWI
period RMB 2
END

## Slide 28
Input-Capture Applications cont’d …
Example-2 of period measurement :
Use the input-capture channel 0 to measure the period of an unknown signal. The program must be able to measure any reasonable period width. Assume that E clock frequency is 24 MHz. Use the number of clock cycles as the unit of the period.
Solution :
We will set the pre-scale factor to 32 and use the clock cycle as the unit of measurement. The period of one clock cycle is 1.33 s. Since the pulse width can be much larger than 216 clock cycles, we will need to keep track of number of times that the TCNT overflows. Each TCNT overflow adds 216 clock cycles to the pulse width.
Let
    ovcnt = TCNT overflow count
    diff = the difference of two consecutive edges
    edge1 = the captured time of 1st edge
    edge2 = the captured time of the 2nd edge

## Slide 29
Input-Capture Applications cont’d …
The pulse width can be calculated by the following equations:
In case 2, the timer overflows at least once even if the pulse width is shorter than 216 clock cycles. Therefore, we need to subtract 1 from the timer overflow count in order to get the correct result.
The pulse width obtained by appending the difference of the two captured edges to the TCNT overflow count.

## Slide 30
Overflow edge1 = A

## Slide 31
Input-Capture Applications cont’d …
Start
yes
overflow ← 0, Disable all interrupts
Set up to capture the rising edge
Clear C0F flag, save 1st captured edge
C0F = 1?
Compute the difference of two edges
C0F = 1?
Combine the results.
Stop
yes
no
no
Clear timer overflow flag
Enable main timer overflow interrupt
yes
Is 2nd edge smaller?
no
overflow ← overflow - 1
Clear TOF flag.
overflow ← overflow + 1
Execute the RTI instruction
Timer overflow interrupt service routine
TOV interrupt
RTN from int.
Logic flow for measuring pulse width of slow signals

## Slide 32
Input-Capture Applications cont’d …
******************************************************************************
* Measuring period of any unknown signal using Input-capture *
******************************************************************************
#include reg9s12.h
ORG $1000
MOVW #tov_is,$3E5E ; set TCNT overflow interrupt vector
MOVB #0,overflow ; clear overflow counter
MOVB #$90,TSCR ; enable timer/counter & fast clear
MOVB #$05,TMSK2 ; disable TCNT overflow interrupt,
* ; set prescaler to 32
CLI ; clear global mask
BCLR TIOS,$01 ; enable input-capture 0
MOVB #$03,TCTL4 ; capture the rising edge of PT0 signal
LDD TC0 ; clear the C0F flag
wait BRCLR TFLG1,$01,wait ; wait for the arrival of 1st rising edge
MOVW TC0,edge1 ; save the 1st edge & clear flag C0F
LDD TCNT ; clear TOF flag
BSET TMSK2,$80 ; enable TCNT overflow interrupt
rep BRCLR TFLG1,$01,rep ; wait for the arrival of falling edge
MOVB #$05,TMSK2 ; disable interrupt
LDD TC0 ; grab the 2nd edge
CPD edge1 ; if 2nd edge lower or same treat it
BLS next1 ; separately
SUBD edge1 ; compute the difference between edges
STD edge1 ; and save it temporarily
JMP next ;

## Slide 33
Input-Capture Applications cont’d …
next1 COM edge1 ; complement edge1 and add it to
COM edge1+1 ; edge2 and save it temporarily
ADDD edge1 ; also decrement overflow count
STD edge1 ;
DEC overflow ;
next SWI
tov_is LDD TCNT ; clear TOF flag
INC overflow ; increment overflow counter
RTI
overflow RMB 1
edge1 FDB 0
END

## Slide 34
HCS12
555 Timer
VOUT
PT0
C = 4.7 F
0.01 F
VCC (5 V)
R2 = 50 kΩ pot
R1 = 1 kΩ
4
6
2
5
1
8
7
3
Input Capture cont’d …
Example:
Write a program to display signal’s period on LCD. To accomplish this you need to do the followings:
    Use 555 chip to generate variable frequency square wave.
    Connect the output to PT0.
    Enable channel 0 as IC and set overflow interrupt of free counter.
    Sample the signal, calculate period/frequency and display on LCD.
    Assemble, download, and run your program.

## Slide 35
Output-Capture Function
The HCS12 has eight output-compare channels. Each channel consists of
  A 16-bit comparator
  A 16-bit compare register TCx, x = 0 … 7 (also used as input capture register)
  An output action pin (PTx – can be pulled up to high, pulled down to low, or toggled)
  An interrupt request circuit
  A forced-compared function (CFORCx)
  Control logic
Operation of the Output-Compare Function
One of the major applications of an output-compare function is performing an action at a specific time in the future (when the 16-bit timer counter reaches a specific value).

## Slide 36
Output-Capture Function cont’d …
The action might be to toggle a signal, turn on a switch, turn off a valve, and so on. To use an output compare function, the user
  Makes a copy of the current contents of the TCNT register
  Adds to this copy a value equal to the desired delay
  Stores the sum into an output-compare register (TCx)
The delay to be added is dependent on the prescaler to TCNT.
The prescaler needs to be set before the delay value is chosen.
The user has the option of specifying the action to be activated on the selected output-compare pin by programming the TCTL1 and TCTL2 registers.

## Slide 37
Output-Capture Function cont’d …
The comparator compares the value of TCNT and that of the specified output-compare register (TCx) in every clock cycle (the clock input to TCNT).
If they are equal, the specified action on the output-compare pin is activated and the associated status bit in TFLG1 will be set to 1.
An interrupt request will be generated if it is enabled.
The 16-bit output-compare register can be read and written any time.
Registers Related to the Output-Compare Function
The actions that can be activated on an output-compare pin are
  Pull-up to high
  Pull-down to low
  Toggle

## Slide 38
Output-Capture Function cont’d …
The action on an OC pin can be selected by programming the TCTL1 and TCTL2 registers as shown below.
When either OMn or OLn is 1, the pin associated with OCn becomes an output tied to OCn regardless of the state of the associated DDRT bit.
OM7
OL7
OM6
OL6
OM5
OL5
OM4
OL4
0
0
0
0
0
0
0
0
Timer Control register 1 (TCTL1)
OM3
OL3
OM2
OL2
OM1
OL1
OM0
OL0
0
0
0
0
0
0
0
0
Timer Control register 2 (TCTL2)
  OMn OLn – output level (n = 0 … 7)
  0 0 : no action (timer disconnected from output pin)
  0 1 : toggle PTn pin
  1 0 : clear PTn pin to 0 (low)
  1 1 : set PTn pin to 1 (high)

## Slide 39
TMSK1 $004C
TFLG1 $004E
16-bit Free Running Counter
Compare
D
M
U
X
Output Compare 0
(bit 1, 0)
0
1
TCTL2 $0049
Interrupt [$FFEE, EF]
(bit 0)
PT0
TC0 $0050 – 51
1
2
3
0
Output-Capture Function cont’d …
TCNT $0044 – 45
Output-Compare Channel-0 Block Diagram

## Slide 40
Output-Capture Applications
Example-1
Generate an active high 1-kHz digital waveform with a 30% duty cycle from the PT0 pin. Use the polling method to check the success of the output-compare operation. The frequency of E clock is 24 MHz.
Solution :
An active high 1-kHz waveform with a 30% duty cycle looks as follows:
The logic flow of this problem is illustrated in the next slide. Suppose that we set the prescale factor to 8 so that the period of the clock input to TCNT is set to 1/3 s. Then the intervals of the PT0 signal to be high and low in one period would be 900 and 2100 clock cycles, respectively.
300 s
700 s

## Slide 41
Output-Capture Applications cont’d …
Start
yes
Select pull high as pin action
Clear C0F flag
C0F = 1?
Select pull low as pin action
Clear C0F flag
Start OC0 output-compare with a delay of 300 s
C0F = 1?
yes
no
no
Start OC0 output-compare with a delay of 700 s.
The program logic flow for digital waveform generation

## Slide 42
Output-Capture Applications cont’d …
#include reg9s12.h
ORG $1000
MOVB #$90,TSCR ; enable TCNT with fast clear
MOVB #$03,TMSK2 ; disable interrupt, set prescale to 8
BSET TIOS,$01 ; select OC on channel 0
MOVB #$02,TCTL2 ; select pull low as pin action
LDD TCNT ; start OC0 operation with 300 s
repeat ADDD #hi_time ;
STD TC0 ;
Low BRCLR TFLG1,$01,Low ; wait until OC0 pin goes high
MOVB #$01,TCTL2 ; select toggle as pin action
LDD TC0 ; start an OC operation with 700 s
ADDD #lo_time ;
STD TC0 ;
High BRCLR TFLG1,$01,high ; wait until OC0 pin goes low
LDD TC0 ; clear flag
JMP repeat

## Slide 43
Output-Capture Applications cont’d …
Example-2
Write a function to generate a time delay that is a multiple of 1 ms. Assume that E clock frequency is 24 MHz. The number of milliseconds is passed in Y register. Also write an instruction sequence to call this function.
Solution :
There are many ways to create a 1-ms time delay using the output-compare function. One method is
  Set the prescaler to TCNT to 64
  Find the number of timer clock cycle to create a 1-ms time delay. That is the number to be added to TC0 register which is N × (64 ÷ 24) = 1000 s → N = 375
  Sit on a gadfly loop to recognize each 1-ms delay
  Repeat the process to create as many ms necessary
  Create a subroutine out of this function
The corresponding assembly function is as follows:.

## Slide 44
Output-Capture Applications cont’d …
LDY #50 ; create 50 ms delay
JSR mildly ;
mildly PSHD ; save content of [D]
MOVB #$90,TSCR ; enable TCNT & fast flag clear
MOVB #$06,TMSK2 ; set prescale to 64
BSET TIOS,$01 ; enable OC0
LDD TCNT ; get the time
rep_ms ADDD #375 ; set the 1-ms on OC register
STD TC0 ;
wait_ms BRCLR TFLG1,$01,wait_ms ; wit for 1-ms
LDD TC0 ; get OC register to add 1-ms
DBNE Y,rep_ms ; repeat as many ms necessary
PULD ; restore content of [D]
RTS

## Slide 45
Output-Capture Applications cont’d …
Example-3
Combine the use of input-capture and output-compare functions to write a program that measures the frequency of an unknown signal attached to PT0 pin. Assume that E clock frequency is 24 MHz.
Solution :
One method for measuring the frequency is using one of the output-compare functions to create a 1-s time interval and keep track of the total number of rising (or falling) edges arrived at the PT0 pin. The number of rising edges arrived in 1-s gives the frequency of the signal. By enabling the PT0 interrupt and writing an interrupt service routine for the PT0 interrupt that increases the edge count, the frequency can be measured.

## Slide 46
Output-Capture Applications cont’d …
#include reg9s12.h
ORG $1000
MOVW #tc0_is,$3E6E ; set up interrupt vector for PT0
MOVB #$90,TSCR ; enable TCNT with fast clear
MOVB #$02,TMSK2 ; no overflow interrupt, set prescale to 4
MOVB #$02,TIOS ; enable IC0 and OC1
MOVB #$01,TCTL4 ; capture the rising edge
LDD TC0 ; clear capture 0 flag
CLI ; enable global interrupt mask
redo MOVB #100,oc_cnt ; prepare OC1 for 100 of 10 ms
MOVW #0,frequency ; initialize frequency count to 0
BSET TMSK1,$01 ; enable IC0 interrupt
LDD TCNT ; start OC1 operation with 10 ms
repeat ADDD #60000 ;
STD TC1 ;
w_lp BRCLR TFLG1,$02,w_lp ; wait until OC1 flag goes high
LDD TC1 ; clear flag & start the next 10 ms
DEC oc_cnt ;
BNE repeat ;
BCLR TMSK1,$01 ; disable IC0 interrupt
LDD frequency ; wait until OC0 pin goes low

## Slide 47
Output-Capture Applications cont’d …
PSHD
LDD #msg ; print the value out
LDX printf ;
JSR 0,X ;
LEAS 2,SP ; balance the stack
JMP redo
SWI
tc0_is LDD TC0 ; clear flag
LDX frequency ; increment frequency count
INX ;
STX frequency ;
RTI ;
oc_cnt RMB 1
frequency RMB 2
msg DB CR,LF
FCC ‘The frequency is %d’
DB CR,LF,0
CR EQU $0D
LF EQU $0A
END

## Slide 48
Output-Capture Applications cont’d …
Use the previous example and this time try to control both input-capture and output-compare through interrupt handler to measures the frequency of an unknown signal attached to PT0 pin. Assume that E clock frequency is 24 MHz
Solution :
In this case, since we are using interrupt for both functions, we need to consider to minimize the number of interrupts for gate keeping (1 second window) so input capture can readily access interrupt. We can accommodate this by choosing prescaler of 128. The clock cycle in this case would be 5 1/3 s. To create a 1 second gate, one need 187,500 clock cycles. This number is larger than 16-bit. Quarter of a second needs 46,875 clock cycle which is manageable. This way OC interrupt will be called 4 times which is tolerable.

## Slide 49
Output-Capture Applications cont’d …
#include reg9s12.h
ORG $1000
MOVW #tc0_is,$3E6E ; set up interrupt vector for PT0
MOVW #tc1_is,$3E6C ; set up interrupt vector for PT1
MOVB #$90,TSCR ; enable TCNT with fast clear
MOVB #$07,TMSK2 ; no overflow interrupt, set prescale to 128
MOVB #$02,TIOS ; enable IC0 and OC1
MOVB #4,oc_cnt ; prepare OC1 for 4 of 250 ms
MOVW #0,frequency ; initialize frequency count to 0
MOVB #$01,TCTL4 ; capture the rising edge
LDD TC1 ; clear OC1 flag
BSET TMSK1,$02 ; enable OC1 interrupt
CLI ; enable global interrupt mask
repeat JMP repeat ; infinite loop
get LDD frequency ; pick up the frequency value in Hex
PSHD ; print the value out
LDD #msg ;
LDX printf ;
JSR 0,X ;
LEAS 2,SP ; balance the stack
SWI

## Slide 50
Output-Capture Applications cont’d …
tc0_is LDD TC0 ; clear flag
LDX frequency ; increment frequency count
INX ;
STX frequency ;
RTI ;
Tc1_is BSET TMSK1,$01 ; allow IC to interrupt
LDD TC1 ; get the value of OC1 register and
ADDD #46875 ; add to it 46875 (1/4 Sec) and
STD TC1 ; put it back
DEC oc_cnt ; decrement ¼ sec from time
BNE done ; if second is not over continue
BCLR TMSK1,$03 ; disable both interrupts
MOVW #get,7,SP ; redirect program to output result
done RTI
oc_cnt RMB 1
frequency RMB 2
msg DB $0D,$0A
FCC ‘The frequency is %d’
DB $0D,$0A,0
printf EQU $EE88
END

## Slide 51
Output-Capture Applications cont’d …
Making Sound Using the Output-Compare Function
Using output-compare function to make sound is easy. A sound can be made by creating a digital waveform of appropriate frequency and using it to drive a speaker or a buzzer. A small speaker of 8-Ω resistance that consumes between 10 mW and 20 mW can produce good quality sound.
Example-4
Describe the circuit for making a sound and write a program that uses an output-compare channel to generate a siren that oscillates between 300 Hz and 1200 Hz.
Solution :
A simple 8-mW speaker (or a buzzer on a demo board) has two terminals: one terminal is for signal input, whereas the other terminal is for ground connection. The circuit connection for siren generation is as follows:
PT5
3.3 F
buzzer

## Slide 52
Output-Capture Applications cont’d …
The algorithm for generating the siren is as follows:
Step 1
Enable an appropriate OC channel (OC5 in this example) to drive the speaker circuit.
Step 2
Start an output-compare operation and enable its interrupt with a delay count equal to half the period of siren.
Step 3
Wait for certain amount of time (say ½ a second). During the waiting period, interrupt will be requested by the output-compare many times. The interrupt service routine simply starts the next output-compare operation and then returns.
Step 4
At the end of the delay, choose a different delay count for the output-compare operation so the siren sound with a different frequency can be generated.
Step 5
Wait for the same amount of time as in step 3. Again, the interrupt caused by the output-compare match will be requested many times. At the end of the delay, switch back to the delay count used in step2.
Step 6
Go to step 2.

## Slide 53
Output-Capture Applications cont’d …
#include reg9s12.h
ORG $1000
MOVW #tc5_is,$3E64 ; set up interrupt vector for OC5
MOVB #$90,TSCR ; enable TCNT with fast clear
MOVB #$03,TMSK2 ; disable interrupt, set prescale to 8
MOVB #$20,TIOS ; enable OC5
MOVB #toggle,TCTL1 ; select toggle for OC5 pin action
LDD #hi_freq ; use high freq delay first
STD delay ; make it available for OC5 handler
LDD TCNT ; start the hi freq sound
ADDD delay ;
STD TC5 ;
MOVB #$20,TFLG1 ; clear OC5 flag
BSET TMSK1,$20 ; enable OC5 interrupt
CLI ; enable global interrupt mask
forever LDY #500 ; wait for half a second
JSR mildly ;
MOVW #lo_freq,delay ; switch to lo freq delay count
LDY #500 ; wait for half a second
JSR mildly ;
MOVW #hi_freq,delay ; switch to hi freq delay count
JMP forever ;

## Slide 54
Output-Capture Applications cont’d …
mildly PSHD ; save content of [D]
MOVB #$90,TSCR ; enable TCNT & fast flag clear
MOVB #$03,TMSK2 ; set prescale to 8
BSET TIOS,$01 ; enable OC0
LDD TCNT ; get the time
rep_ms ADDD #3000 ; set the 1-ms on OC register
STD TC0 ;
wait_ms BRCLR TFLG1,$01,wait_ms ; wait for 1-ms
LDD TC0 ; get OC register to add 1-ms
DBNE Y,rep_ms ; repeat as many ms necessary
PULD ; restore content of [D]
RTS
tc5_is LDD TC5 ; get time & clear flag
ADDD delay ; set the next interval
STD TC5 ;
RTI
delay RMB 2 ; storage for the delay count of TC5
hi_freq EQU 1250 ; delay count for 1200 Hz (1:8 prescaler)
lo_freq EQU 5000 ; delay count for 300 Hz (1:8 prescaler)
toggle EQU $04 ; value to toggle TC5 pin

## Slide 55
Output-Capture Applications cont’d …
Making Music Using the Output-Compare Function
A siren can be considered as a song with only two notes. A song can be created by modifying the siren program. To make the switching of frequency easier, the whole score should be stored in a table. A note has two components: one is the frequency and the other is the duration. The duration of a quarter note is about 0.4 second. The duration of other notes can be derived proportionally. To play a song from the speaker, one places the frequencies and durations of all the notes in a music score in a table. For every note, the user program uses the output-compare function to generate the digital waveform with the specified frequency and duration.
Example-5
Write a program to play “The Star-Spangled Banner”. Assume that the demo board is running with a 24-MHz E clock.
Solution :
The following assembly program plays the national anthem.

## Slide 56
Output-Capture Applications cont’d …
Lets look at A4 which is middle A:
  A4 = 440 Hz, which means its period is approximately 2,273 s.
  Half the period would be 1,136 s.
  If we are working with a prescaler of 8, it means every clock cycle will be 1/3 of a s.
  To generate A4 we need to add 3,409 to output compare register every time.
  In other words, the delay counter for A4 is 3,409.
  Based on this calculation, one can generate all the delay counts for all the notes and tabulate it for use.
  The following table does this for the pre scaler of 8.

## Slide 57
Output-Capture Applications cont’d …
Note | Freq (Hz) | Count | Note | Freq (Hz) | Count | Note | Freq (Hz) | Count
C3 | 130.81 | 11,467 | C4 | 261.63 | 5,733 | C5 | 523.25 | 2,867
C#3/Db3 | 138.59 | 10,823 | C#4/Db4 | 277.18 | 5,412 | C#5/Db5 | 554.37 | 2,706
D3 | 146.83 | 10,216 | D4 | 293.66 | 5,108 | D5 | 587.33 | 2,554
D#3/Eb3 | 155.56 | 9,643 | D#4/Eb4 | 311.13 | 4,821 | D#5/Eb5 | 622.25 | 2,411
E3 | 164.81 | 9,101 | E4 | 329.63 | 4,551 | E5 | 659.26 | 2,275
F3 | 174.61 | 8,591 | F4 | 349.23 | 4,295 | F5 | 698.46 | 2,148
F#3/Gb3 | 185.00 | 8,108 | F#4/Gb4 | 369.99 | 4,054 | F#5/Gb5 | 739.99 | 2,027
G3 | 196.00 | 7,653 | G4 | 392.00 | 3,827 | G5 | 783.99 | 1,913
G#3/Ab3 | 207.65 | 7,224 | G#4/Ab4 | 415.30 | 3,612 | G#5/Ab5 | 830.69 | 1,806
A3 | 220.00 | 6,818 | A4 | 440.00 | 3,409 | A5 | 880.00 | 1,705
A#3/Bb3 | 233.08 | 6,436 | A#4/Bb4 | 466.16 | 3,218 | A#5/Bb5 | 932.33 | 1,609
B3 | 246.94 | 6,074 | B4 | 493.88 | 3,037 | B5 | 987.77 | 1,519
Music Note Frequencies

## Slide 58
Output-Capture Applications cont’d …
Note | Freq (Hz) | Count | Note | Freq (Hz) | Count | Note | Freq (Hz) | Count
C6 | 1046.50 | 1,433 | C7 | 2093.00 | 717 |  |  | 
C#6/Db6 | 1108.73 | 1,353 | C#7/Db7 | 2217.46 | 676 |  |  | 
D6 | 1174.66 | 1,277 | D7 | 2349.32 | 638 |  |  | 
D#6/Eb6 | 1244.51 | 1,205 | D#7/Eb7 | 2489.02 | 603 |  |  | 
E6 | 1318.51 | 1,138 | E7 | 2637.02 | 569 |  |  | 
F6 | 1396.91 | 1,074 | F7 | 2793.83 | 537 |  |  | 
F#6/Gb6 | 1479.98 | 1,014 | F#7/Gb7 | 2959.96 | 507 |  |  | 
G6 | 1567.98 | 957 | G7 | 3135.96 | 478 |  |  | 
G#6/Ab6 | 1661.22 | 903 | G#7/Ab7 | 3322.44 | 451 |  |  | 
A6 | 1760.00 | 852 | A7 | 3520.00 | 426 |  |  | 
A#6/Bb6 | 1864.66 | 804 | A#7/Bb7 | 3729.31 | 402 |  |  | 
B6 | 1975.53 | 759 | B7 | 3951.07 | 378 |  |  | 
Music Note Frequencies

## Slide 59
Output-Capture Applications cont’d …
As far as note duration is concerned, if quarter note is approximately 0.4 s, then we can find delay counts for a whole, half, quarter, eighth, and sixteenth for the case of prescaler of 8.
To accomplish this, we use OC0 to generate a 1 ms delay and run it as many time as needed for the duration of the note.
Whole note is 1600 ms, half note 800 ms, quarter note 400 ms, eighth note 200 ms, and sixteenth note is 100 ms.
Based on these explanations, the following is the code that will play the Star-Spangled Banner tune.

## Slide 60
Output-Capture Applications cont’d …
#include reg9s12.h
ORG $1000
MOVW #tc5_is,$3E64 ; set up interrupt vector for OC5
MOVB #$90,TSCR ; enable TCNT with fast clear
MOVB #$03,TMSK2 ; disable interrupt, set prescaler to 8
MOVB #$20,TIOS ; enable OC5
MOVB #toggle,TCTL1 ; select toggle for OC5 pin action
MOVB #2,rep_cnt ; play the song twice
twice LDX #score ; use as a pointer to score table
MOVB #notes,ip ; total number of notes in the song
MOVW 2,X+,delay ; start with zeroth note
LDD TCNT ; play the first note
ADDD delay ;
STD TC5 ;
MOVB #$20,TFLG1 ; clear OC5 flag
BSET TMSK1,$20 ; enable OC5 interrupt
CLI ; enable global interrupt mask
forever LDY 200,X ; get the duration
JSR mildly ;
MOVW 2,X+,delay ; get the next note
DEC ip ; all notes are played?
BNE forever ;

## Slide 61
Output-Capture Applications cont’d …
DEC rep_cnt ; if not done reestablish pointer
BEQ done ;
JMP twice ;
done SWI
mildly PSHD ; save content of [D]
MOVB #$90,TSCR ; enable TCNT & fast flag clear
MOVB #$03,TMSK2 ; set prescale to 8
BSET TIOS,$01 ; enable OC0
LDD TCNT ; get the time
rep_ms ADDD #3000 ; set the 1-ms on OC register
STD TC0 ;
wait_ms BRCLR TFLG1,$01,wait_ms ; wait for 1-ms
LDD TC0 ; get OC register to add 1-ms
DBNE Y,rep_ms ; repeat as many ms necessary
PULD ; restore content of [D]
RTS
tc5_is LDD TC5 ; get time & clear flag
ADDD delay ; set the next interval
STD TC5 ;
RTI

## Slide 62
Output-Capture Applications cont’d …
delay RMB 2 ; storage for the delay count of TC5
rep_cnt RMB 1 ; number of times song to be repeated
Ip RMB 1 ; number of notes to be played
notes EQU 101 ; number of notes
toggle EQU $04 ; value to toggle TC5 pin
G3 EQU 7653 ; delay count to generate G3 note (1:8 prescaler)
B3 EQU 6074 ; delay count to generate B3 note (1:8 prescaler)
C4 EQU 5733 ; delay count to generate C4 note (1:8 prescaler)
C4S EQU 5412 ; delay count to generate C4S note (1:8 prescaler)
D4 EQU 5108 ; delay count to generate D4 note (1:8 prescaler)
E4 EQU 4551 ; delay count to generate E4 note (1:8 prescaler)
F4 EQU 4295 ; delay count to generate F4 note (1:8 prescaler)
F4S EQU 4054 ; delay count to generate F4S note (1:8 prescaler)
G4 EQU 3827 ; delay count to generate G4 note (1:8 prescaler)
A4 EQU 3409 ; delay count to generate A4 note (1:8 prescaler)
B4F EQU 3218 ; delay count to generate B4F note (1:8 prescaler)
B4 EQU 3037 ; delay count to generate B4 note (1:8 prescaler)
C5 EQU 2867 ; delay count to generate C5 note (1:8 prescaler)
D5 EQU 2554 ; delay count to generate D5 note (1:8 prescaler)
E5 EQU 2275 ; delay count to generate E5 note (1:8 prescaler)
F5 EQU 2148 ; delay count to generate F5 note (1:8 prescaler)

## Slide 63
Output-Capture Applications cont’d …
* Frequency of each note
score DW D4,B3,G3,B3,D4,G4,B4,A4,G4,B3,C4S
DW D4,D4,D4,B4,A4,G4,F4S,E4,F4S,G4,G4,D4,B3,G3
DW D4,B3,G3,B3,D4,G4,B4,A4,G4,B3,C4S,D4,D4,D4
DW B4,A4,G4,F4S,E4,F4S,G4,G4,D4,B3,G3,B4,B4
DW B4,C5,D5,D5,C5,B4,A4,B4,C5,C5,C5,B4,A4,G4
DW F4S,E4,F4S,G4,B3,C4S,D4,D4,G4,G4,G4,F4S
DW E4,E4,E4,A4,C5,B4,A4,G4,G4,F4S,D4,D4
DW G4,A4,B4,C5,D5,G4,A4,B4,C5,A4,G4
* Duration of each note
duration DW 300,100,400,400,400,800,300,100,400,400,400
DW 800,200,200,600,200,400,800,200,200,400,400,400,400,400
DW 300,100,400,400,400,800,300,100,400,400,400,800,200,200
DW 600,200,400,800,200,200,400,400,400,400,400,200,200
DW 400,400,400,800,200,200,400,400,400,800,400,600,200,400
DW 800,200,200,400,400,400,800,400,400,400,200,200
DW 400,400,400,400,200,200,200,200,400,400,200,200
DW 600,200,200,200,800,200,200,600,200,400,800
END

## Slide 64
Output-Capture Applications cont’d …
There are at least three drawbacks in using this method to play a song:
  Contiguous identical notes become one note. This problem can be solved by inserting a short period of silence between two contiguous identical notes.
  A periodic square waveform is only an approximation to an actual note. Those who have learned communication theory know that a periodic square waveform also contains harmonics with higher frequencies. The solution to this problem is the use of N-stage Johnson Counter to convert the square wave into sine wave.
  There is no loudness control. Using the PWM function rather than the output-compare function and adjusting the duty cycle of each note is one possible solution to the problem.

## Slide 65
N-stage Johnson Counter
  There are several ways of generating sine waves.
  As a viable alternative, output compares module of timer/counter subsystem can be used in conjunction with N-stage Johnson Counters to generate sine waves with different frequencies.
  To generate and transmit a sine wave, the Johnson counter is almost ideal.
  This counter is actually just a shift register whose output is inverted, then shifted back into it.
  A 4-bit Johnson counter is shown in the next slide
Output-Capture Applications cont’d …

## Slide 66
D
D
D
D
Reset
22 KW
33 KW
Clock
VOUT
33 KW
Output-Capture Applications cont’d …
By clearing all four flip-flops, the following sequence of values will circulate through them:
  L L L L
  H L L L
  H H L L
  H H H L
  H H H H
  L H H H
  L L H H
  L L L H

## Slide 67
Although the wave will look like a stair-step approximation to a sine, it is free of the lower harmonics and can be filtered if necessary.
    Note! using more accurate values of resistors and a longer shift register, it is possible to eliminate as much of the low-order harmonics as desired before filtering.
In the case of four-stage Johnson counter, if a sine wave with frequency of ‘F’ is desired, the counter needs to be clocked with a square wave whose frequency is 8F.
Output compare module can be used to generate the square wave clock for the counter. The number ‘N’ to be added to the output compare register every time would be 24,000,000/(16F) given that E clock is running at 24 MHz.
Output-Capture Applications cont’d …

## Slide 68
Using OC7 to control Multiple Output-Compare Functions
  The output-compare function OC7 is special because it can control up to eight output-compare functions at the same time.
  The register OC7M specifies the output-compare channels to be controlled by OC7.
  The value that any PTx (x = 0 …7) pin to assume when the value of TC7 equals that of TCNT is specified by the OC7D register.
  To control an output-compare pin using OC7, the user sets the corresponding bit in OC7M.
  When a successful OC7 compare is made, each affected pin assumes the value of the corresponding bit of OC7D.
Output-Capture Applications cont’d …
OC7M7
OC7M6
OC7M5
OC7M4
OC7M3
OC7M2
OC7M1
OC7M0
0
0
0
0
0
0
0
0
Output-Compare 7 Mask Register (OC7M)
  OC7Mn n = 0 … 7
  0 = PTn pin is not affected by OC7 function.
  1 = a successful OC7 action will override a successful OC6 – OC0 compare action during the same cycle and the OCn action taken will depend on the corresponding OC7D bit.

## Slide 69
16-bit Free Running Counter
Compare
Output Compare 7 Register
D
D
D
D
D
PA7
PA6
PA5
PA4
PA0
TC7 $005E-5F
OC7M $0042
OC7D $0043
Interrupt [$FFE8, E9]
(bit 7)
TFLG1 $004E
TMSK1 $004C
TCNT $0044-45
Output-Capture Applications cont’d …
Notes: M is which one you are enabling
The flips flops are extra, the input are to

## Slide 70
Output-Capture Applications cont’d …
Example-6
What value should be written into OC7M and OC7D if one wants pins PT2, PT3, and PT4 to assume the values of 1, 0, and 1, respectively, when OC7 compare succeeds?
Solution :
Bits 4, 3, and 2 of OC7M must be set to 1, and bits 4, 3, and 2 of OC7D should be set to 1, 0, and 1, respectively. The following instruction sequence will set up these values:
MOVB #$1C,OC7M
MOVB #$14,OC7D
The ability to control multiple output-compare pins is very useful in applications that require multiple actions to be triggered simultaneously in the near future.
Notes: OC7D is to data. Allows you to set up to 8 output compar

## Slide 71
Output-Capture Applications cont’d …
Example-7
Suppose that there is an application that requires the following operations to be triggered 50 ms later:
    Turn off the light controlled by the TC5 pin
    Turn on the temperature sensor controlled by TC4 pin
    Turn off the heater controlled by the TC3 pin
    Turn on the music controlled by the TC2 pin
Write an instruction sequence to perform the desired operation.
Solution :
The values to be written into OC7M and OC7D are $3C and $14, respectively. Set the prescaler to TCNT to 64. Then the value to be added to create a 50-ms delay can be computed as follows:
MOVB #$90,TSCR ; enable TCNT and fast timer flag clear
MOVB #$06,TMSK2 ; set prescaler to 64
MOVB #$3C,OC7M
MOVB #$14,OC7D
LDD TCNT
ADDD #18750 ; (24000000 ÷ 64)  0.05 = 18,750
STD TC7 ; start the OC7 operation
;need to set up a wait instruction
CLR OC7M
0
0
1
1
1
1
0
0
OC7M =
= $3C
0
0
0
1
0
1
0
0
OC7D =
= $14
Notes: You can use the OC7D and OC7E as a switch to enable and disable certain things.

## Slide 72
Forced Output-Compare
  There may be an application in which the user requires an output-compare pin action to occur immediately instead of waiting for a match between TCNT and the proper output-compare register.
  This situation arises in the spark-timing control in some automotive engine control applications.
  To use the forced output-compare mechanism, the user would write to the CFORC register with 1’s in the bit positions corresponding to the output-compare channels to be forced.
  At the next timer count after the write to CFORC, the forced channels will trigger their programmed pin actions to occur.
  The forced actions are synchronized to the timer counter clock input.
  The forced output-compare signal causes pin action but does not affect the timer flag or generate interrupt.
  Normally, the forced mechanism would not be used in conjunction with the automatic pin action that toggles the corresponding output-compare pin.
Output-Capture Applications cont’d …

## Slide 73
Output-Capture Applications cont’d …
FOC7
FOC6
FOC5
FOC4
FOC3
FOC2
FOC1
FOC0
0
0
0
0
0
0
0
0
Contents of the CFORC Register
  FOCn n = 0 … 7
  0 = no effect on corresponding OC.
  1 = the channel will be triggered at the next timer count based on their pin action set up.
Register | Bit Position | Value | Action to be Triggered
TCTL1 TCTL2 | 7 6 5 4 3 2 1 0 7 6 5 4 3 2 1 0 | 1 1 0 1 0 1 1 0 0 1 1 0 1 1 1 0 | Set the PT7 pin to high Toggle the PT6 pin Toggle the PT5 pin Pull the PT4 pin to low Toggle the PT3 pin Pull the PT2 pin to low Set the PT1 pin to high Pull the PT0 pin to low
Pin Actions on PT7 – PT0 Pins

## Slide 74
The Alarm Clock
Use output compare 2 module to keep track of the time, in minutes, up to a day of the week.
The user must be able to set the time and set the alarm at anytime. Time and alarm set up must be capable of fast and slow set up.
The user should be able to turn the alarm ON or OFF. Also alarm should have snooze capability.
Use the LCD module to display time, alarm ON/OFF, and set time/alarm. The following is a way of displaying time on LCD:
      Wed 11:24 am
      Alarm OFF
or
      Sunday 15:45 
The colon needs to blink at the rate of ½ second.
Output-Capture Applications cont’d …
Notes: We are going to use 2 inturpt output com 4 and output com 5 (for the speaker) . You want to minimize the amount of time that you are going to the inturpt.
Setting up how to define a minute by messing with the clock of the cpu. For instance you will be using 128 for the inturpt in order to get 1 min.

## Slide 75
Output-Capture Applications cont’d …
Solution :
One way to accommodate all the requirements of this project is to incorporate 3 switches and 3 push-buttons.
The switches will be used for time set, alarm set, and alarm ON/OFF.
The three push-buttons facilitate the function of snooze as well as setting week day, hour, minute, and am/pm (if necessary).
Since OC5 is already connected to speaker, it will be used to generate alarm. This can be accomplished using interrupt.
Note that time keeping is done through interrupt handler of OC2, therefore, microcontrollers main task is to continuously scan the switches and push-buttons and perform appropriate function based on their state.
It is necessary to decide on the rate of timer counter clock. Since we are going to use at least two interrupt handlers, it makes sense to minimize the number of interrupts. This translates to using lower clock rate.

## Slide 76
Output-Capture Applications cont’d …
For this reason, the prescaler of 128 is selected.
Given the prescaler, what is the largest unit delay that multiple integer of it generates exact second?
      (24,000,000 ÷ 128) ÷ 46,875 = 4
If we assume every match on OC2 is a tick, then we need 4 ticks to elapse a second and 240 ticks to constitute a minute.
Note that to generate a 1 kHz square wave for buzzer, the value to be added to OC5 register is 94.
In the next couple of slides, the skeleton of OC2 handler is discussed.
Notes: We need
3 dip switches set time; set alarm; Alarm on/off
3 push buttons,
24 MHz / 128 => 128 / 24 *10 ^-6 * N = 250000 x 10^-6 (Solve for N); N = 46875 ( N will fit into 2 bytes) You can use 4 inturpts to get a sec
You will need 240 ticks to get a min, Ticks are seconds.
Every 2 ticks is a half a second in order for us to make the : blink
To make buzzer work we need to make N1 set to 94
Varibles:
Hour DB 0
Min DB 0
AHOUR

## Slide 77
tc2_is LDD TC2 ; read OC2 register & clear the flag
ADDD #46875 ; add 1/4 of a second
STD TC2 ;
DEC ticks ; decrement ticks
BRSET ticks,$01,cont ; is it multiple of 2?
blink {refresh LCD} ; else, blink colon
cont LDAB ticks ; is it a minute?
BNE roll ; if not exit
MOVB #240,ticks ; otherwise, reestablish ticks
LDD hour ; get hour/minute
INCB ; increment minute
CMPB #60 ; if less than 60 go and
BLO hr_min ; restore hour/minute
CLRB ; if 60, clear minute and
INCA ; increment hour
CMPA #24 ; if less than 24 go and
BLO hr_min ; restore hour/minute
CLRA ; if 24, clear hour and then
hr_min STD hour ; restore
BNE check ; if day is not over, check alarm
INC day ; increment day and if over
LDAA day ; restart week day
CMPA #7 ;
BLO check ;
CLR day ;
Output-Capture Applications cont’d …
Notes: BRSET will check for the least sig bit, in order to see if it is even or odd
In cont
If tick is not zero it will come back. If it is Equal to zero then it will move another 240 ticks for next min.

## Slide 78
Output-Capture Applications cont’d …
check {check if alarm is ON} ;
{if not go to roll} ;
LDD hour ; check if time and alarm time the same
CPD alarm ;
BNE roll ; if not end handler routine
{turn alarm on} ; else, turn alarm on
roll RTI
tc5_is LDD TC5 ; read OC5 register & clear the flag
ADDD #94 ; create 1/2 millisecond interval
STD TC5 ;
RTI

## Slide 79
Output-Capture Applications cont’d …
Start
yes
Initialize and start the System
Time set switch ON?
Set Alarm
no
no
Set Time
Alarm set switch ON?
yes
Alarm ON?
no
Set Alarm ON
yes

## Slide 80
Input-Capture/Output-Compare Application
Example: Write a program that counts the number of times that pushbutton SW5 has been pressed in one minute and display the result.
Solution:
  Use an output-compare channel to generate a 1 minute window;
  Use an input-capture channel to count number of times that SW5 has been pressed within the 1 minute window.
  Print out the result with appropriate message.
SW5
PH0
IC?
PT?

## Slide 81
#include reg9s12.h
ORG $1000
MOVW #tc0_is,$3E6E ; set up interrupt vector for IC0
MOVW #tc1_is,$3E6C ; set up interrupt vector for OC1
MOVB #$90,TSCR ; enable TCNT with fast clear
MOVB #$07,TMSK2 ; disable interrupt, set prescaler to 128
MOVB #$02,TIOS ; enable OC1
MOVB #$01,TCTL4 ; select pos. edge for IC0 pin
MOVB #0,count ; clear counter
MOVB #240,ticks ; set ticks for 1 minute
{ask user if ready to start}
MOVB #$03,TFLG1 ; clear flags
BSET TMSK1,$03 ; enable interrupts
CLI ; enable global interrupt
wait BRSET TMSK1,$03,wait ; wait till minute is over
{send out value of count}
SWI

## Slide 82
tc1_is LDD TC1 ; read OC1 register & clear the flag
ADDD #46875 ; add 1/4 of a second
STD TC1 ;
DEC ticks ; decrement ticks
BNE roll ;
CLR TMSK1 ; disable both interrupts
roll RTI
tc0_is LDD TC0 ; read OC0 to clear the flag
INC count ; increment counter
RTI