## Slide 1: Overview of HCS12 Parallel Ports
A HCS12 device may have from 48 to 144 pins arranged in 3 to 12 I/O ports and packaged either as quad flat pack (QFP) or a low-profile quad flat pack (LQFP) package.
Quad Flat Pack - QFP
Low-profile Quad Flat Pack - LQFP

## Slide 2
The pins of an I/O port are often multiplexed with one or more peripheral functions (e.g., timer or serial peripheral interface).
When a peripheral function is enabled, that pin may not be used as a general-purpose I/O pin.
General-purpose I/O pins can be considered the simplest of peripherals. They allow the microcontroller to monitor and control other devices.
I/O ports are all 8-bit long. However, all bits of every port is not available to the user based on the functionality of the port and the package used.
The number of pins available in each I/O port for the HCS12 MCU is listed below:
Overview of HCS12 Parallel Ports Cont’d …

## Slide 3
Overview of HCS12 Parallel Ports Cont’d …
Port Name | No. of Pins | Pin Name
A B E H J K M P S T PAD1,PAD0 L U V W | 8 8 8 8 4 7 8 8 8 8 16 8 8 8 8 | PA7~PA0 PB7~PB0 PE7~PE0 PH7~PH0 PJ7~PJ0 PK7~PK0 PM7~PM0 PP7~PP0 PS7~PS0 PT7~PT0 PAD15~PAD0 PL7~PL0 PU7~PU0 PV7~PV0 PW7~PW0

## Slide 4
Overview of HCS12 Parallel Ports Cont’d …
Each I/O port has several associated registers to support its operation and these registers must be dealt with when performing I/O operations by specifying the address of a register in order to read from it or write into it.
A better way is to use the EQU directive (in assembly language) to equate a symbolic name to the address of a given register so that the symbolic name can be used to access it.
For example:
PORTA EQU $00
MOVB #$FF,PORTA
Physical Address

## Slide 5
Overview of HCS12 Parallel Ports Cont’d …
The file Reg9S12.h that contains the EQU directive for all peripheral registers has been provided on the example Folder of DRAGON12.
Include this file with your program, then you will be able to use symbolic names to access all peripheral registers.
For example:
#include C:\DARGON12\examples\Reg9S12.h
ORG $1000

## Slide 6: Port Registers
All I/O ports (except PAD0 & PAD1) have an associated data direction register (DDR) and a data register.
To configure a pin for output, write a 1 to the corresponding bit in the data direction register.
To configure a pin for input, write a 0 to the corresponding bit in the data direction register.
MOVB #$00,DDRA ;configure port A for input
LDAA PORTA ;reads a byte into A from port A
MOVB #$FF,DDRB ;configure port B for output
MOVB #$A5,PORTB ;output $A5 to port B

## Slide 7
Port Registers Cont’d …
A complete list of symbolic names for port data registers is shown in the following table:
Port Name | Data Register Name
A B E H J K M P S T PAD1,PAD0 L U V W | PORTA1 PORTB1 PORTE1 PTH PTJ PORTK1 PTM PTP PTS PTT PORTAD1,PORTAD0 PTL2 PTU2 PTV2 PTW2
1 PORTA, PORTB, PORTE, and PORTK are also referred to as PTA, PTB, PTE, and PTK in the Reg9S12.h file.
2 Port L, U, V, & W are available in H-family devices only.

## Slide 8
GND
Dip Switches
LEDs
7-segment LEDs
2-line, 16 character/line LCD
H-Bridge Connections
Reset
Speaker
Small Breadboard
Keypad
Mode indicator switches
LCD contrast Pot
Abort
Push buttons

## Slide 10
Port A & B:
when configured in single-chip mode, these two ports are used as general-purpose I/O ports.
Every single pin can be configured as input or output.
In expanded mode, both port A & B are used as time-multiplexed address/data bus extension.
In expanded mode, port A carries the time-multiplexed upper address and data signals, whereas port B carries the time-multiplexed lower address and data signals.
Port B
Port A
A0/D0
A7/D7
A8/D8
A15/D15

## Slide 11
Port E:
Port E pins are used for bus control and interrupt service request signals.
When the pin is not used for one of these special functions, it can be used as a general-purpose I/O.
Two of the port E pins (PE[0:1]) can only be used for input, and the states of these pins can be read in the port data register even when they are used for IRQ and XIRQ.
PE0 – XIRQ
PE1 – IRQ
PE2 – R/W
PE3 – LSTRB – TAGLO
PE4 – ECLK
PE5 – MODA – IPIPE0
PE6 – MODB – IPIPE1
PE7 – NOACC – XCLKS
Port E pins and their alternate functions

## Slide 12
The PE7 pin serves three functions:
A general-purpose I/O pin
A signal that indicates the MCU is not accessing external memory
A signal that selects between the external clock or crystal oscillator signal as the clock input to the HCS
The PE6 and PE5 pins serve three functions:
A general-purpose I/O pins (in single-chip mode)
Signals that set the operation mode of the HCS12 after reset
Instruction queue tracking signals (in expanded mode)
The PE4 pin has two functions:
A general-purpose I/O pin (in single-chip mode)
The E clock output (in expanded mode)
Port E Cont’d …

## Slide 13
The PE3 pin has three functions:
A general-purpose I/O pin (in single-chip mode)
The LCD front-plane segment driver output pin (in H family)
The low-byte strobe signal to indicate the type of access (in expanded mode)
The PE2 pin has two functions:
A general-purpose I/O pins (in single-chip mode)
A signal to indicate whether the current bus cycle is a read cycle or a write cycle (in expanded mode)
The PE1 pin has two functions:
A general-purpose I/O pin
The IRQ input
The PE0 pin has two functions:
A general-purpose I/O pin
The XIRQ input
Port E Cont’d …

## Slide 14
Port E Registers:
In addition to the DDRE and PORTE registers, port E also has the following registers:
  Port E assignment register (PEAR)
  Mode register (MODE)
  Pull-up control register (PUCR)
  Reduced drive register (RDRIV)
  External bus interface control register (EBICTL)
Port E Assignment Register (PEAR)
In expanded mode, this register assigns the function of each port E pin. The PEAR register is not accessible for reads or writes in peripheral mode. The pin assignment for PEAR register is as follows:

## Slide 15
NOACCE
0
PIPOE
NECLK
LSTRE
0
RDWE
0
0
1
2
3
4
5
6
7
NOACCE: No Access output enable. Can be read/written any time.
  0 = PE7 is used as general-purpose I/O pin.
  1 = PE7 is output and indicates whether the cycle is a CPU free cycle.
PIPOE: Pipe signal output enable.
  In normal modes, write once. Special modes, write anytime except the first time. This bit has no effect on single-chip mode.
  0 = PE[6:5] are general-purpose I/O.
  1 = PE[6:5] are outputs and indicate the state of the instruction queue.
NECLK: No External E clock. Can be read any time.
  In expanded modes, write to this bit has no effect. E clock is required for de-multiplexing the external address. NECLK can be written once in normal single-chip mode and can be written anytime in special single-chip mode.
  0 = PE4 is the external E clock.
  1 = PE4 is a general-purpose I/O pin.
Port E Registers Cont’d …

## Slide 16
RDWE: Read/Write enable. Can be read any time.
  In normal modes, write once. Special modes, write anytime. This bit has no effect in single-chip modes.
  0 = PE2 is a general-purpose I/O pin.
  1 = PE2 is configured as the R/W pin. In single-chip modes, RDWE has no effect and PE2 is a general-purpose I/O pin.
  R/W used for external writes. After reset in normal expanded mode, it is disabled. If needed, it should be enabled before any external writes.
MODE Register
This register establishes the operation mode and other miscellaneous functions (i.e., internal visibility and emulation of ports E and K). The pin assignment for MODE register is as follows:
LSTRE: Low strobe (LSTRB) enable. Can be read any time.
  In normal modes, write once. Special modes, write anytime. This bit has no effect on single-chip modes or normal expanded narrow modes.
  0 = PE3 is a general-purpose I/O pin.
  1 = PE3 is configured as the LSTRB bus-control output, provided that the HCS12 is not in single-chip or normal expanded narrow modes.
Port E Registers Cont’d …

## Slide 17
MODC, MODB, MODA: mode select bits.
  000 = special single-chip mode
  001 = emulation narrow mode
  010 = special test mode
  011 = emulation wide mode
  100 = normal single-chip mode
  101 = normal expanded narrow mode (external data bus memory is 8-bit)
  110 = special peripheral mode
  111 = normal expanded wide mode (external memory data bus is 16-bit)
IVIS: internal visibility.
  0 = no visibility of internal bus operations on external bus.
  1 = internal bus operations are visible on external bus.
EMK: emulate port K.
  0 = PORTK and DDRK are in the memory map and port K can be used for general I/O.
  1 = if in any expanded mode, PORTK and DDRK are removed from memory map.
MODC
MODB
MODA
0
IVIS
0
EMK
EME
0
1
2
3
4
5
6
7
Port E Registers Cont’d …

## Slide 18
Pull-Up Control Register (PUCR)
This register is used to select the pull-up resistors for the pins associated with the core part. The MC9S12DP256 has ports A, B, E, and K in its core part. This register can be written at any time. The pin assignment for PUCR register is as follows:
PUPKE
0
0
PUPEE
0
0
PUPBE
PUPAE
0
1
2
3
4
5
6
7
PUPKE: pull-up port K enable.
  0 = pull-up resistors of port K are disabled.
  1 = pull-up resistors of port K are enabled.
PUPEE: pull-up port E enable.
  0 = pull-up resistors of port E are disabled.
  1 = pull-up resistors of port E are enabled.
EME: emulate port E.
  0 = PORTE and DDRE are in the memory map and port E can be used for general I/O
  1 = in any expanded mode or special peripheral mode, PORTE and DDRE are removed from memory map, which allows the user to emulate the function of these registers externally.
Port E Registers Cont’d …

## Slide 19
Reduced Drive Register (RDRIV)
This register is used to select drive for the pins associated with the core ports, which gives reduced power consumption and reduced RFI with a slight increase in transition time, a feature used on ports that have a light loading. This register is not in the memory map in expanded mode. The pin assignment for RDRIV register is as follows:
RDPK
0
0
RDPE
0
0
RDPB
RDPA
0
1
2
3
4
5
6
7
PUPBE: pull-up port B enable.
  0 = pull-up resistors of port B are disabled.
  1 = pull-up resistors of port B are enabled.
PUPAE: pull-up port A enable.
  0 = pull-up resistors of port A are disabled.
  1 = pull-up resistors of port A are enabled.
Port E Registers Cont’d …

## Slide 20
External Bus Interface Control Register (EBICTL)
Only the bit 0 (ESTR) of this register is implemented. It controls the stretching of the external E clock. When the ESTR bit is set to 0, the E clock is free-running and does not stretch (lengthen). When the HCS12 is interfacing with a slower memory drive, then the E clock can be lengthened (stretch its high interval) by setting this bit.
RDPK: reduced drive of port K.
  0 = all port K pins have full drive enabled.
  1 = all port K pins have reduced drive enabled.
RDPE: reduced drive of port E.
  0 = all port E pins have full drive enabled.
  1 = all port E pins have reduced drive enabled.
RDPB: reduced drive of port B.
  0 = all port B pins have full drive enabled.
  1 = all port B pins have reduced drive enabled.
RDPA: reduced drive of port A.
  0 = all port A pins have full drive enabled.
  1 = all port A pins have reduced drive enabled.
Port E Registers Cont’d …

## Slide 21
Port K:
Port K has a data register (PORTK) and a data direction register (DDRK).
In expanded mode, port K carries the expanded address XADDR14~XADDR19, emulated chip select (ECS), and external chip select (XCS) signals.
At the rising edge of the RESET signal, the state of the PK7 pin is latched to the ROMON bit of the MISC register. If this bit is 1, the on-chip flash memory will be enabled in the extended mode. This bit is forced to 1 in the single-chip modes.
PK0 – X14
PK1 – X15
PK2 – X16
PK3 – X17
PK4 – X18
PK5 – X19
PK6 – XCS (only available in H subfamily)
PK7 – ECS/ROMON
Port K pins and their alternate functions

## Slide 22
Port T:
Port T has a port I/O register (PTT), port data direction register (DDRT), port input register (PTIT), reduced drive register (RDRT), pull-up device enable register (PERT), and port polarity select register (PPST).
The PTIT register allows one to read back the status of port T pins. This register can also be used to detect overload or short circuit conditions on output pins.
The RDRT register configures the drive strength of each port output pin as either full or reduced current. If a port pin is used as input, this bit is ignored. The reduced drive feature for each pin can be enabled individually.
RDRT7
RDRT6
RDRT5
RDRT4
RDRT3
RDRT2
RDRT1
RDRT0
0
0
0
0
0
0
0
0
RDRT[7:0]: reduced drive port T.
  0 = full drive strength at output.
  1 = associated pin devices at about 1/3 of the full drive strength.

## Slide 23
The PERT register configures whether a pull-up or pull-down device is enabled if the port is used as input. Each pin’s pull-up or pull-down device can be enabled individually. No pull-up or pull-down device is enabled out of reset.
PERT7
PERT6
PERT5
PERT4
PERT3
PERT2
PERT1
PERT0
0
0
0
0
0
0
0
0
PERT[7:0]: pull device enable port T.
  0 = pull-up or pull-down is disabled.
  1 = either pull-up or pull-down is enabled.
The PPST register selects whether a pull-down or pull-up device is connected to the pin. This register has an effect on input pins only.
PPST7
PPST6
PPST5
PPST4
PPST3
PPST2
PPST1
PPST0
0
0
0
0
0
0
0
0
Port T Cont’d …

## Slide 24
PT0 – IOC0
PT1 – IOC1
PT2 – IOC2
PT3 – IOC3
PT4 – IOC4
PT5 – IOC5
PT6 – IOC6
PT7 – IOC7
Port T pins and their alternate functions
The pin function of port T are shown below. In addition to being used as general I/O pins, port T pins can also be used as input capture or output compare action pins.
PPST[7:0]: pull polarity select port T.
  0 = a pull-up device is connected to the associated port T pin, if enabled by the associated bit in register PERT and if the port is used as input or as wired-or output.
  1 = a pull-down device is connected to the associated port T pin, if enabled by the associated bit in register PERT and if the port is used as input.
Port T Cont’d …

## Slide 25
Port S:
Port S has a port S Wired-OR mode register (WOMS) in addition to all the registers associated with port T (PTS, DDRS, PTIS, RDRS, PERS, and PPSS).
Each bit of WOMS register configures the associated output pin as wired-OR. The contents of this register is shown below.
WOMS7
WOMS6
WOMS5
WOMS4
WOMS3
WOMS2
WOMS1
WOMS0
0
0
0
0
0
0
0
0
WOMS[7:0]: wired-OR mode port S.
  0 = output buffers operate as push-pull output.
  1 = output buffers operate as open-drain output.
The contents of PTIS, RDRS, PERS, and PPSS are identical to those of port T. Port S pins can be used as general I/O pins or serial interface signals.
PS0 – RXD0
PS1 – TXD0
PS2 – RXD1
PS3 – TXD1
PS4 – MISO0
PS5 – MOSI0
PS6 – SCK0
PS7 – SS0

## Slide 26
Ports H, J, and P:
These three I/O ports have the same set of registers associated with them.
All of the pins associated with these three ports have edge-triggered interrupt capability in the wired-OR fashion.
The SPI function pins can be routed to ports H and P.
The routing of SPI functions done by programming the MODRR register.
Each of these three ports has eight associated registers:
  Port I/O register (PTH, PTJ, PTP)
  Port input register (PTIH, PTIJ, PTIP)
  Port data direction register (DDRH, DDRJ, DDRP)
  Port reduced drive register (RDRH, RDRJ, RDRP)
  Port pull device enable register (PERH, PERJ, PERP)
  Port polarity select register (PPSH, PPSJ, PPSP)
  Port interrupt enable register (PIEH, PIEJ, PIEP)
  Port interrupt flag register (PIFH, PIFJ, PIFP)

## Slide 27
PIEH7
PIEH6
PIEH5
PIEH4
PIEH3
PIEH2
PIEH1
PIEH0
0
0
0
0
0
0
0
0
PIEH[7:0]: interrupt enable port H.
  0 = interrupt is disabled.
  1 = interrupt is enabled.
All except the last two registers have been discussed. The contents of the port H Interrupt Enable register and port H Interrupt Flag register are shown below:
PIFH7
PIFH6
PIFH5
PIFH4
PIFH3
PIFH2
PIFH1
PIFH0
0
0
0
0
0
0
0
0
PIFH[7:0]: interrupt flag port H.
  0 = no active edge pending.
  1 = active edge has occurred (writing a ‘1’ clears the associated flag).
Ports H, J, & P Cont’d …

## Slide 28
The interrupt enable as well as the sensitivity to rising or falling edges can be individually configured on a per pin basis.
If a pin’s pull-down device is enabled, then the interrupt is rising-edge triggered. Otherwise, it is falling-edge triggered.
All 8-bits/pins of the port share the same interrupt vector. Interrupts can be used with the pin configured as inputs or outputs.
PH0 – MISO1/KWH0
PH1 – MOSI1/KWH1
PH2 – SCK1/KWH2
PH3 – SS1/KWH3
PH4 – MISO2/KWH4
PH5 – MOSI2/KWH5
PH6 – SCK2/KWH6
PH7 – SS2/KWH7
PJ0 – KWJ0
PJ1 – KWJ1
PJ6 – KWJ6/RXCAN0
PJ7 – KWJ7/TXCAN0
PP0 – MISO1/PWM0
PP1 – MOSI1/PWM1
PP2 – SCK1/PWM2
PP3 – SS1/PWM3
PP4 – MISO2/PWM4
PP5 – MOSI2/PWM5
PP6 – SCK2/PWM6
PP7 – SS2/PWM7
Port H
Port J
Port P
Ports H, J, & P Cont’d …

## Slide 29
Ports AD0 and AD1:
HCS12 have implemented two 8-channel A/D converters.
These two ports are analog input interface to the analog-to-digital subsystem.
When analog-to-digital functions are not enabled, these two ports are available for general-purpose I/O.
Since these ports can not be used as output, there are no data direction registers associated with them.
The ports have no resistive input loads and no reduced drive controls.
Corresponding data registers for these two ports are called PTAD0 and PTAD1.
To be able to use these ports as digital input, each port has a ATD digital input enable register (ATD0DIEN and ATD1DIEN).
In order to use an A/D pin as a digital input, its associated bit in this register needs to be set to 1.

## Slide 30
IEN7
IEN6
IEN5
IEN4
IEN3
IEN2
IEN1
IEN0
0
0
0
0
0
0
0
0
IENx[7:0]: ATD digital input enable on channel x.
  0 = disable digital input buffer to PTADx pin.
  1 = enable digital input buffer to PTADx pin.
Electrical & Timing Considerations for I/O Interfacing:
Voltage-level compatibility.
Current Drive compatibility.
Timing compatibility.
D
Clk
Q
Q
tsu
thd
D
Clk
Set-up time
Hold time

## Slide 31
What is the difference between a Line and a Bus?
D
Clk
Q
Q
D
Clk
Q
Q
D
Clk
Q
Q
D
Clk
Q
Q
Level-triggered
‘Latch’
Edge-triggered
‘Register’
Register A
D
Clk
Q
Q

## Slide 32
TFR A,B
D
Clk
Q
Q
D
Clk
Q
Q
A
B
C1
C3
C4
C2
C1 | C2 | C3 | C4
L | L | L | L
L | H | L | L
L | H | H | L
L | L | L | L
At any given time, only one driver drives the bus.

## Slide 33: Interfacing with Simple I/O Devices
Interfacing with LEDs:
The LEDs are often used to indicate the system operation mode, whether power is turned on, whether system operation is normal, and so forth.
An LED can illuminate when it is forward biased and has sufficient current flowing through it.
The current required to light a LED may range from a few to more than 10 mA.
The voltage drop across the LED can range from 1.6 V to more than 2.2 V.
There are three different methods for interfacing with LEDs.
The first two methods are only recommended for use with LEDs that need only 1 to 2 mA to produce enough brightness.

## Slide 34: Interfacing with Simple I/O Devices cont’d …
74HC04
Port Pin
Port Pin
Port Pin
VCC
VCC
R3
R2
R1
1. Positive Direct Drive
2. Inverse Direct Drive
3. Buffered Drive
An LED connected to a CMOS inverter through a current
The circuit 3 is recommended for use with LEDs that need larger current to light.
Dragon12 has provided 8 LEDs which are connected to Port B.
Bit 1 of port J is used to enable and disable these connections. If it is set to 0 will enable this function.

## Slide 35: Interfacing with Simple I/O Devices cont’d …
*****************************************************************************************
* Function: Makes port B as a binary counter and displays it on LEDs. *
*****************************************************************************************
#include reg9s12.h
org $1000 ; program code
start ldaa #$FF
staa ddrb ; make port B an output port
staa ddrp ; make port P an output port
staa ptp ; turn off 7-segment LED display
bset ddrj,$02 ; make bit 1 of port j output
bclr ptj,$02 ; clear bit 1 of port j to enable LEDs
back inca ; create a binary counter with 100 ms
staa portb ; delay between counts
jsr d_100ms ;
jmp back ;
d_100ms ldab #100 ; delay 100 ms
dly1 ldy #6000 ; 6000 x 4 = 24,000 cycles = 1ms
dly dey ; 1 cycle
bne dly ; 3 cycles
dbne b,dly1 ; continue till it is 100 ms
rts
end

## Slide 36
Interfacing with Simple I/O Devices cont’d …
************************************************************************************
* Function: Turns LEDs ON and OFF one at a time every 100 ms. *
************************************************************************************
#include reg9s12.h
org $1000 ; program code
start ldaa #$ff
staa ddrb ; make port B an output port
staa ddrp ; make port P an output port
staa ptp ; turn off 7-segment LED display
bset ddrj,$02 ; make bit 1 of port j output
bclr ptj,$02 ; clear bit 1 of port j to enable LEDs
************************************************************************************
* Function: Turns LEDs ON and OFF one at a time every 100 ms. *
************************************************************************************
#include reg9s12.h
org $1000 ; program code
start ldaa #$ff
staa ddrb ; make port B an output port
staa ddrp ; make port P an output port
staa ptp ; turn off 7-segment LED display
bset ddrj,$02 ; make bit 1 of port j output
bclr ptj,$02 ; clear bit 1 of port j to enable LEDs
movb #1,portb ; start with most right LED
repeat ldaa #7 ; shift left 7-times with100 ms
bb jsr d_100ms ; delay between moves
lsl portb ;
dbne a,bb ;
ldaa #7 ; shift right 7-times with100 ms
bb1 jsr d_100ms ; delay between moves
lsr portb ;
dbne a, bb1 ;
jmp repeat ; repeat process

## Slide 37: Interfacing with Simple I/O Devices cont’d …
************************************************************************************
* Function: Turns LEDs ON and OFF one at a time every 100 ms. *
************************************************************************************
#include reg9s12.h
org $1000 ; program code
start ldaa #$ff
staa ddrb ; make port B an output port
staa ddrp ; make port P an output port
staa ptp ; turn off 7-segment LED display
bset ddrj,$02 ; make bit 1 of port j output
bclr ptj,$02 ; clear bit 1 of port j to enable LEDs
************************************************************************************
* Function: Turns LEDs ON and OFF one at a time every 100 ms. *
************************************************************************************
#include reg9s12.h
org $1000 ; program code
start ldaa #$ff
staa ddrb ; make port B an output port
staa ddrp ; make port P an output port
staa ptp ; turn off 7-segment LED display
bset ddrj,$02 ; make bit 1 of port j output
bclr ptj,$02 ; clear bit 1 of port j to enable LEDs
repeat ldy #led_tbl ; create a moving light with 100 ms
back movb 1,y+,portb ; delay between moves
pshy ;
jsr d_100ms ;
puly ;
cpy #led_tbl+14 ;
bne back ;
bra repeat ;
*

## Slide 38: Interfacing with Simple I/O Devices cont’d …
d_100ms ldab #100 ; delay 100 ms
dly1 ldy #6000 ; 6000 x 4 = 24,000 cycles = 1ms
dly dey ; 1 cycle
bne dly ; 3 cycles
dbne b,dly1 ; continue till it is 100 ms
rts
led_tbl fcb $80,$40,$20,$10,$08,$04,$02,$01
fcb $02,$04,$08,$10,$20,$40
end
Interfacing with DIP Switches:
A switch is probably the simplest input device we can find.
To make input more efficient, a set of eight switches are organized as a dual-in-package (DIP) is often used.
A DIP package can be connected to any input port with eight pins.
Dragon12 board uses port H to connect the DIP switches.
When the switch is closed the associated port H input is 0.

## Slide 39
Interfacing with Simple I/O Devices cont’d …
PH0 PH1 PH2 PH3 PH4 PH5 PH6 PH7
HCS12
SW DIP-8
VCC
10 kΩ
SW5
SW4
SW3
SW2
Schematic of Push Buttons and DIP Switches on Dragon12 Board

## Slide 40
Interfacing with Simple I/O Devices cont’d …
Example: Write a program that displays a binary counter on the 8-LEDs. Program should control the speed of the counter through DIP switches and terminate any time push button SW5 is pressed.
**********************************************************************************************************************
*Program creates binary counter and displays it on LEDs. The speed of the counter is controlled*
* by DIP switches. The program will terminates as soon as push button SW5 is pressed. *
**********************************************************************************************************************
#include reg9s12.h
org $1000 ; program code
start ldaa #$ff
staa ddrb ; make port B an output port
staa ddrp ; make port P an output port
staa ptp ; turn off 7-segment LED display
bset ddrj,$02 ; make bit 1 of port j output
bclr ptj,$02 ; clear bit 1 of port j to enable LEDs
clr ddrh ; make port H an input port
back inca ; create a binary counter with as many ms
staa portb ; delay between counts as DIP switches are
jsr d_100ms ; indicating. Stop when push button
brset pth,$01,back ; SW5 is pressed.
swi

## Slide 41
Interfacing with Seven-Segment Displays:
Seven-segment displays are often used when the embedded product needs to display only a few digits.
Seven-segment displays are mainly used to display digits and small subset of letters.
Although a HCS12 device has enough current to drive a seven-segment display, it is not advisable to do so when the controller needs to drive many other devices.
d_100ms ldab pth ; read DIP switches for no. of ms delay
dly1 ldy #6000 ; 6000 x 4 = 24,000 cycles = 1ms
dly dey ; 1 cycle
bne dly ; 3 cycles
dbne b,dly1 ; continue till it is 100 ms
rts
end
Interfacing with Simple I/O Devices cont’d …

## Slide 42: Interfacing with Simple I/O Devices cont’d …
Port B derives a common-cathode seven-segment display through the buffer chip 74HC244.
The light patterns corresponding to ten BCD (decimal) digits are shown in the following table.
The numbers in table require that segments a~g be connected from PB0~PB6 of the output port B.
PB0
PB1
PB2
PB3
PB4
PB5
PB6
a
b
c
d
e
f
g
b
a
c
d
e
f
g
Common Cathode
300 Ω each
74HC244
HCS12

## Slide 43
BCD Digit | g f e d c b a Pb6 pb5 pb4 pb3 pb2 pb1 pb0 | Corresponding Hex Number
0 1 2 3 4 5 6 7 8 9 | 0 1 1 1 1 1 1 0 0 0 0 1 1 0 1 0 1 1 0 1 1 1 0 0 1 1 1 1 1 1 0 0 1 1 0 1 1 0 1 1 0 1 1 1 1 1 1 0 1 0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1 0 1 1 1 1 | $3F $06 $5B $4F $66 $6D $7D $07 $7F $6F
Interfacing with Simple I/O Devices cont’d …
When an application needs to display multiple BCD digits, the time-multiplexing technique is used.
An example of the circuit that displays 4 BCD digits is shown in next slide.
The common-cathode of the display is connected to the collector of an NPN transistor.

## Slide 44
PB0 …………… PB6
300 Ω each
74HC244
HCS12
a
b
c
d
e
f
g
PP0
PP1
PP2
PP3
R
R
R
R
2N2222
2N2222
2N2222
2N2222
Common Cathodes
#4
#3
#2
#1
IMAX = 70 mA
Interfacing with Simple I/O Devices cont’d …

## Slide 45
Interfacing with Simple I/O Devices cont’d …
When a port P pin voltage is low, the connected NPN transistor will be driven into saturation region.
The common cathode of the display then will be pulled-down to about 0.1 volt, allowing the display to be lighted.
By turning ON and OFF these four transistors multiple time per second, multiple digits can be displayed.
When all segments of a display is ON they draw about 70 mA of current that 2N2222 transistor is capable of sinking that current.
To ensure the saturation mode for the transistor, a value of several hundred to 1 kΩ resistor is needed for ‘R’.
The following two programs will demonstrate the use of the seven-segment module on Dragon12.

## Slide 46
**********************************************************************************
* Set third 7-segment LED to value 4 *
**********************************************************************************
#include reg9s12.h ; include register equates
org $1000
ldaa #$ff ; turn off 7-segment display
staa ddrb ; portb = output
staa ddrp ; portp = output
staa ptp ; portp = 11111111 - all 7-segments are off
ldaa #$66 ; seven segment code for digit '4'
staa portb
bset ptp,$01 ; turn off digit 1
bset ptp,$02 ; turn off digit 2
bclr ptp,$04 ; turn on digit 3
bset ptp,$08 ; turn off digit 4
swi
*** segment pattern ***
zero fcb $3f,$06,$5b,$4f,$66,$6d,$7d,$07 ; 0-7
* 0, 1, 2, 3, 4, 5, 6, 7
fcb $7f,$6f,$77,$7c,$39,$5e,$79,$71 ; 8-$0f
* 8, 9, A, b, C, d, E, F
end
Interfacing with Simple I/O Devices cont’d …

## Slide 47
Interfacing with Simple I/O Devices cont’d …
*********************************************************************************************
* Set 7-segment module to display '6125' *
*********************************************************************************************
#include reg9s12.h ; include register equates
org $1000
ldaa #$ff ; [A] = 11111111
staa ddrb ; portb = output
staa ddrp ; portp = output
staa ptp ; turn off all 7-segment displays
repeat ldaa #$7d ; seven segment for digit '6'
staa portb ; send it to 7-segment
bclr ptp,$01 ; turn on digit 1
jsr d_1ms ; keep it ON for 1 ms
bset ptp,$01 ; turn off digit 1
ldaa #$06 ; seven segment for digit '1'
staa portb ; send it to 7-segment
bclr ptp,$02 ; turn on digit 2
jsr d_1ms ; keep it ON for 1 ms
bset ptp,$02 ; turn off digit 2
ldaa #$5b ; seven segment for digit '2'

## Slide 48
staa portb ; send it to 7-segment
bclr ptp,$04 ; turn on digit 3
jsr d_1ms ; keep it ON for 1 ms
bset ptp,$04 ; turn off digit 3
ldaa #$6d ; seven segment for digit '5'
staa portb ; send it to 7-segment
bclr ptp,$08 ; turn on digit 4
jsr d_1ms ; keep it ON for 1 ms
bset ptp,$08 ; turn off digit 4
jmp repeat
d_1ms ldy #6000 ; 6000 x 4 = 24,000 cycles = 1ms
dly dey ; 1 cycle
bne dly ; 3 cycles
rts
* segment pattern
zero fcb $3f,$06,$5b,$4f,$66,$6d,$7d,$07 ; 0-7
* 0, 1, 2, 3, 4, 5, 6, 7
fcb $7f,$6f,$77,$7c,$39,$5e,$79,$71 ; 8-$0f
* 8, 9, A, b, C, d, E, F
end
Interfacing with Simple I/O Devices cont’d …

## Slide 49
*************************************************************************************
* Set 7-seg module to Count 0 to F in Hex while scrolling to right and * *wrapping around it will terminate once push button SW5 is pressed. *
*************************************************************************************
#include reg9s12.h ; include register equates
org $1000
ldaa #$ff ; turn off 7-segment display
staa ptp ; portp = 11111111
bset ddrj,$02 ; bit 2 of port j is output
bset ptj,$02 ; turn off LEDs
staa ddrb ; portb = output
staa ddrp ; portp = output
repeat ldy #zero ; start at digit 0 - 3
Interfacing with LCD cont’d …
Write an assembly program to set the 7-segment module to count 0 to F in HEX while scrolling to right and wrapping around. The program should terminate once push button SW5 is pressed.

## Slide 50
new movb 0,y,dig1 ; load initial values into
movb 1,y,dig2 ; four 7-segments
movb 2,y,dig3 ;
movb 3,y,dig4 ;
ldab #25 ; repeat 25 times
redo ldaa dig1 ; get unit digit
staa portb ; send it to 7-segment
bclr ptp,$01 ; turn on digit 4
jsr d_1ms ; delay 1 ms
bset ptp,$01 ; turn off digit 4
ldaa dig2 ; get 10 digit
staa portb ; send it to 7-segment
bclr ptp,$02 ; turn on digit 3
jsr d_1ms ; delay 1 ms
bset ptp,$02 ; turn off digit 3
ldaa dig3 ; get 100 digit
Interfacing with LCD cont’d …

## Slide 51
staa portb ; send it to 7-segment
bclr ptp,$04 ; turn on digit 2
jsr d_1ms ; delay 1 ms
bset ptp,$04 ; turn off digit 2
ldaa dig4 ; get 1000 digit
staa portb ; send it to 7-segment
bclr ptp,$08 ; turn on digit 1
jsr d_1ms ; delay 1 ms
bset ptp,$08 ; turn off digit 1
dbne b,redo
iny ; scroll down by one
cpy #zero+16 ; is pointer out of range?
bne new ; if no, then continue
jmp repeat ; if yes, then re-initialize
done swi
Interfacing with LCD cont’d …

## Slide 52
d_1ms brclr pth,$01,done
ldx #6000 ; 6000 x 4 = 24,000 cycles = 1ms
dly dex ; 1 cycle
bne dly ; 3 cycles
rts
*** segment pattern ***
zero fcb $3f,$06,$5b,$4f,$66,$6d,$7d,$07 ; 0-7
* 0, 1, 2, 3, 4, 5, 6, 7
fcb $7f,$6f,$77,$7c,$39,$5e,$79,$71 ; 8-$0f
* 8, 9, A, b, C, d, E, F
fcb $3f,$06,$5b
* 0, 1, 2
dig1 rmb 1
dig2 rmb 1
dig3 rmb 1
dig4 rmb 1
end
Interfacing with LCD cont’d …

## Slide 53
#4
#3
#2
#1
ad3
ad2
ad1
Y
dig1
dig2
dig3
dig4
Write an assembly program to set the 7-segment module to count up to ‘9999’.

## Slide 54
********************************************************************************
* Set 7-segment module to Count up to '9999' *
********************************************************************************
#include reg9s12.h ; include register equates
org $1000
ldaa #$ff ; [A] = 11111111
staa ddrb ; portb = output
staa ddrp ; portp = output
staa ptp ; turn off 7-segment displays
ldy #zero
sty ad3
sty ad2
sty ad1
movb 0,y,dig4
movb #0,dig3
movb #0,dig2
movb #0,dig1
Interfacing with Simple I/O Devices cont’d …

## Slide 55
Interfacing with Simple I/O Devices cont’d …
repeat ldab #10
redo ldaa dig4 ; get unit digit
staa portb ; send it to 7-segment
bclr ptp,$08 ; turn on digit 4
jsr d_1ms ; delay 1 ms
bset ptp,$08 ; turn off digit 4
ldaa dig3 ; get 10th digit
staa portb ; send it to 7-segment
bclr ptp,$04 ; turn on digit 3
jsr d_1ms ; delay 1 ms
bset ptp,$04 ; turn off digit 3
ldaa dig2 ; get 100th digit
staa portb ; send it to 7-segment
bclr ptp,$02 ; turn on digit 2
jsr d_1ms ; delay 1 ms
bset ptp,$02 ; turn off digit 2
ldaa dig1 ; get 1000th digit
staa portb ; send it to 7-segment
bclr ptp,$01 ; turn on digit 1
jsr d_1ms ; delay 1 ms
bset ptp,$01 ; turn off digit 1
dbne b,redo

## Slide 56
Interfacing with Simple I/O Devices cont’d …
iny ; increment unit digit
cpy #zero+10 ; as long as not 10, continue refreshing
bne cont4 ;
ldy ad3 ; get 10th digit
iny ; increment 10th digit
cpy #zero+10 ; as long as not 10, re-initialize pointer
bne cont3 ; for unit digit and continue refreshing
ldy ad2 ; get 100th digit
iny ; increment 100th digit
cpy #zero+10 ; as long as not 10, re-initialize pointer
bne cont2 ; for unit & 10th digits, continue refreshing
ldy ad1 ; get 1000th digit
iny ; increment 1000th digit
cpy #zero+10 ; as long as not 10, re-initialize pointer for
bne cont1 ; unit, 10th, & 100th digits, continue refreshing
swi
cont1 movb 0,y,dig1 ; update 1000th digit
sty ad1 ; save 1000th digit pointer
ldy #zero ; update digit 100th to zero
cont2 movb 0,y,dig2 ;
sty ad2 ; save 100th digit pointer
ldy #zero ; update digit 10th to zero
cont3 movb 0,y,dig3 ;
sty ad3 ; save 10th digit pointer
ldy #zero ; update unit digit to zero
cont4 movb 0,y,dig4 ;
jmp repeat ; go back to refresh all 4 digits

## Slide 57
Interfacing with Simple I/O Devices cont’d …
d_1ms ldx #6000 ; 6000 x 4 = 24,000 cycles = 1ms
dly dex ; 1 cycle
bne dly ; 3 cycles
rts
* segment pattern
zero fcb $3f,$06,$5b,$4f,$66,$6d,$7d,$07 ; 0-7
* 0, 1, 2, 3, 4, 5, 6, 7
fcb $7f,$6f,$77,$7c,$39,$5e,$79,$71 ; 8-$0f
* 8, 9, A, b, C, d, E, F
dig1 rmb 1
dig2 rmb 1
dig3 rmb 1
dig4 rmb 1
ad3 rmb 2
ad2 rmb 2
ad1 rmb 2
end

## Slide 58
****************************************************************************************************
* Set 7-segment module to Count up to '9999' *
****************************************************************************************************
#include C:\Dragon12P\Examples\Reg9s12.h ; include register equates
ORG $1000
MOVB #$FF,ddrb ; portb = output
MOVB #$FF,ddrp ; portp = output
MOVB #$FF,ptp ; turn off 7-segment displays
CLR ddrh ; porth = input
BSET ddrj,$02 ; bit 1 of port j is output
BSET ptj,$02 ; disable LEDs

## Slide 59
LDAA dig1 ; get rid of leading zeros
CMPA #$3F ;
BNE cont ;
MOVB #0,dig1 ;
LDAA dig2 ;
CMPA #$3F ;
BNE cont ;
MOVB #0,dig2 ;
LDAA dig3 ;
CMPA #$3F ;
BNE cont ;
MOVB #0,dig3 ;
cont LDAB pth ; set the speed
redo MOVB dig4,portb ; get unit digit
BCLR ptp,$08 ; turn on digit 4
JSR d_1ms ; delay 1 ms
BSET ptp,$08 ; turn off digit 4
MOVB dig3,portb ; get 10th digit
BCLR ptp,$04 ; turn on digit 3
JSR d_1ms ; delay 1 ms
BSET ptp,$04 ; turn off digit 3
MOVB dig2,portb ; get 100th digit
BCLR ptp,$02 ; turn on digit 2
JSR d_1ms ; delay 1 ms
BSET ptp,$02 ; turn off digit 2
MOVB dig1,portb ; get 1000th digit
BCLR ptp,$01 ; turn on digit 1
JSR d_1ms ; delay 1 ms
BSET ptp,$01 ; turn off digit 1
DBNE b,redo

## Slide 60
LDX N
INX
STX N
CPX #9999
LBLS next
JMP restrt
done SWI
d_1ms BRCLR pth,$01,done
LDX #6000 ; 6000 x 4 = 24,000 cycles = 1ms
dly DEX ; 1 cycle
BNE dly ; 3 cycles
RTS
* segment pattern
zero DB $3f,$06,$5b,$4f,$66,$6d,$7d,$07 ; 0-7
* 0, 1, 2, 3, 4, 5, 6, 7
DB $7f,$6f,$77,$7c,$39,$5e,$79,$71 ; 8-$0f
* 8, 9, A, b, C, d, E, F
dig1 RMB 1
dig2 RMB 1
dig3 RMB 1
dig4 RMB 1
N RMB 2
END

## Slide 61
Interfacing with Liquid Crystal Displays (LCDs):
Although seven-segment displays are easy to use, they are bulky and quite limited in the set of characters that they can display.
Liquid Crystal Displays come in handy when the application requires the display of many characters.
LCD has the following advantages:
    High contrast
    Low power consumption
    Small footprint
    Ability to display both characters and graphics
The basic construction of an LCD is shown on next slide. The most common type of LCD allows light to pass through when activated.
When a voltage is applied across the segment, an electrostatic field is set up that aligns the crystal in the liquid.

## Slide 62
Glass
Segment
Frontplane
Backplane
Black cardboard backing or light source
Liquid crystal
A Liquid Crystal Display (LCD)
Interfacing with LCD cont’d …
Although LCDs can display graphics and characters, only character-based LCD controller is used on Dragon12 board.
The Hitachi HD44780, one of the most popular LCD display controllers, is used on Dragon12.

## Slide 63
HD44780U
Com1
Com8
Com9
Com16
Seg1
Seg5
Seg6
Seg10
Seg200
40 Characters
Interfacing with LCD cont’d …
Line 1
Line 2

## Slide 64
CONTROLLER
LSI
HD44780U
Segment Driver  4
LCDP (FRD7069)
COM 16
SEG 40
SEG 160
4
DB7
DB0
E
R/W
RS
VEE
VCC
VSS
Block diagram of a HD44780U-based LCD kit
Interfacing with LCD cont’d …
The HD44780U LCD Controller:
The block diagram of an LCD kit that incorporates the HD44780U controller is shown.

## Slide 65
Pin No. | Symbol | I/O | Function
1 2 3 4 5 6 7 8 9 10 11 12 13 14 | VSS VCC VEE RS R/W E DB0 DB1 DB2 DB3 DB4 DB5 DB6 DB7 | -- -- -- I I I I/O I/O I/O I/O I/O I/O I/O I/O | Power supply (GND) Power supply (+5 V) Contrast adjust 0 = instruction input, 1 = data input 0=write to LCD, 1=read from LCD Enable signal Data bus line 0 Data bus line 1 Data bus line 2 Data bus line 3 Data bus line 4 Data bus line 5 Data bus line 6 Data bus line 7
Pin assignment for displays with no more than 80 characters
Interfacing with LCD cont’d …

## Slide 66
Pin No. | Symbol | I/O | Function
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 | DB7 DB6 DB5 DB4 DB3 DB2 DB1 DB0 E1 R/W RS VEE VSS VCC E2 N.C. | I/O I/O I/O I/O I/O I/O I/O I/O I I I -- -- -- I -- | Data bus line 7 Data bus line 6 Data bus line 5 Data bus line 4 Data bus line 3 Data bus line 2 Data bus line 1 Data bus line 0 Enable signal row 0 and 1 0=write to LCD, 1=read from LCD 0 = instruction input, 1 = data input Contrast adjust (GND) Power supply (+5 V) Power supply Enable signal row 2 and 3
Pin assignment for displays with more than 80 characters
Interfacing with LCD cont’d …

## Slide 67
Interfacing with LCD cont’d …
The HD44780U provides a set of instructions for user to setup the LCD parameters.
The operations performed by these instructions are summarized on a table and will be presented in upcoming slides.
The HD44780U can be configured to control 1-line, 2-line, and 4-line LCDs.
The mappings of the character positions on the LCD screen and the Display Data RAM (DDRAM) addresses are not sequential and are shown in a table in upcoming slides.
To better understand these tables, one needs to get familiar with memory allocations and different registers on board of the LCD controller.
Display Data RAM (DDRAM) – stores display data represented in 8-bit character codes. Its extended capacity is 80  8 bits, or 80 characters.

## Slide 68
Interfacing with LCD cont’d …
Character Generator ROM (CGROM) – The character generator ROM generates 5  8 or 5  10 dot character patterns from 8-bit character codes. It can generate 208 (58) dot character patterns and 32 (510) dot character patterns.
Character Generator RAM (CGRAM) – The user can rewrite character patterns into the CGRAM by programming. For 5  8 fonts, eight character patterns can be written, and for 5  10 fonts, four character patterns can be written.
Instruction Register (IR) – The IR is an 8-bit register which stores instruction codes, such as “display clear” and “cursor move”, and address information for DDRAM and CGRAM.
Data Register (DR) – The DR is an 8-bit register that is used to transfer data from microcontroller into LCD controller. The IR and DR registers are distinguished by the RS signal.

## Slide 69
Instruction | Code | Description | Execution time
 | RS R/W B7 B6 B5 B4 B3 B2 B1 B0 |  | 
Clear display | 0 0 0 0 0 0 0 0 0 1 | Clears display and returns cursor to the home position (address 0). | 1.64 ms
Cursor home | 0 0 0 0 0 0 0 0 1 * | Returns cursor to home position. Also returns display being shifted to the original position. DDRAM content remains unchanged. | 1.64 ms
Entry mode set | 0 0 0 0 0 0 0 1 I/D S | Sets cursor move direction (I/D); specifies to shift the display (S). These operations are performed during data read/write. | 40 s
Display on/off control | 0 0 0 0 0 0 1 D C B | Sets on/off of all display (D), cursor on/off (C), and blink of cursor position character (B). | 40 s
Cursor/display shift | 0 0 0 0 0 1 S/C R/L * * | Sets cursor-move or display-shift (S/C), shift direction (R/L). DDRAM content remains unchanged. | 40 s
Function set | 0 0 0 0 1 DL N F * * | Sets interface data length (DL), number of display line (N), and character font (F). | 40 s
Set CGRAM address | 0 0 0 1 CGRAM address | Sets the CGRAM address. CGRAM data are sent and received after this setting. | 40 s
Set DDRAM address | 0 0 1 DDRAM address | Sets the DDRAM address. DDRAM data are sent and received after this setting. | 40 s
Read busy flag & address counter | 0 1 BF CGRAM/DDRAM address | Reads busy flag (BF) indicating internal operation being performed and reads CGRAM or DDRAM address counter contents (depending on previous instruction. | 0 s
Write CGRAM or DDRAM | 1 0 write data | Write data to CGRAM or DDRAM | 40 s
Read from CG/DDRAM | 1 1 read data | Read data from CGRAM or DDRAM | 40 s

## Slide 70
Interfacing with LCD cont’d …
Busy Flag (BF) – The HD44780U has a busy flag to indicate whether the current internal operation is complete. When BF is 1, the controller is still busy with an internal operation. When RS = 0 and R/W = 1, the busy flag is output to the DB7.
Address Counter (AC) – The HD44780U uses a 7-bit address counter to keep track of the address of the next DDRAM or CGRAM location to be accessed. When an instruction is written into the IR register, the address information contained in the instruction is transferred to the AC register. After writing or reading of DDRAM or CGRAM, the content of the AC register is automatically incremented by 1.
Instruction Description:
  Clear Display – Clears the whole DDRAM and sets the address counter to 0. It reconfigures the LCD to its initial mode and sets I/D to 1 (increment mode).

## Slide 71
Interfacing with LCD cont’d …
  Return Home – sets DDRAM address 0 into the address counter and returns to its original status if it was shifted. The DDRAM contents are not changed.
  Entry Mode Set – The I/D bit of the instruction controls increment/decrement which in turn controls cursor going to right or left. The S bit controls the shifting of the LCD display. S=1→ display shifts, S=0 → display does not shift.
  Display ON/OFF Control – This instruction has three bit parameters: D, C, and B. D=1→ display is turned ON, C=1 → cursor is turned on, B=1 → cursor blinks.
  Cursor or Display Shift – This instruction shifts the cursor position to the right or left without writing or reading display data. Shifting is controlled by two bits as its shown.
S/C | R/L | Operation
0 0 1 1 | 0 1 0 1 | Shifts the cursor position to the left. (AC is decremented by 1). Shifts the cursor position to the right. (AC is incremented by 1). Shifts the entire display to the left. The cursor follows the display shift. Shifts the entire display to the right. The cursor follows the display shift.

## Slide 72
Interfacing with LCD cont’d …
  Function Set – This instruction allows the user to set the interface data length, select the number of display lines, and select the character fonts. There are three bit variables in this instruction:
  DL = 1 → data length 8-bit, DL = 0 → data length 4-bit (DB7 – DB4)
  N = 0 → 1-line display is selected, N = 1 → 2-line display is selected
  F = 0 → 5  8 font is selected, F =1 → the 5  10 font is selected.
  Set CGRAM Address – This instruction contains the CGRAM address to be set into the address counter.
  Set DDRAM Address – This instruction allows the user to set the address of the DDRAM (in address counter).
  Read Busy Flag and Address – This instruction reads the busy flag (BF) and the address counter. The BF flag indicates whether the LCD controller is still executing the previously received instruction.

## Slide 73
Bit Name | Settings
I/D S D C B S/C R/L DL N F BF | 0=decrement cursor position 1=increment cursor position 0 = no display shift 1 = display shift 0 = display off 1 = display on 0 = cursor off 1 = cursor on 0 = cursor blink off 1 = cursor blink on 0 = move cursor 1 = shift display 0 = shift left 1 = shift right 0 = 4-bit interface 1 = 8-bit interface 0 = 1/8 or 1/11 duty (1 line) 1 = 1/16 duty (2 lines) 0 = 58 dots 1 = 510 dots 0 = can accept instruction 1 = internal operation in progress
LCD Instruction bit names
Interfacing with LCD cont’d …
The next slide represents the DDRAM address usage both for 1-line display as well as 2-line display.

## Slide 74
Display Size | Visible | 
 | Character Positions | DDRAM Addresses
1  8 1  16 1  20 1  24 1  32 1  40 | 00..07 00..15 00..19 00..23 00..31 00..39 | 0 00..0 07 0 00..0 0F 0 00..0 13 0 00..0 17 0 00..0 1F 0 00..0 27
Display Size | Visible | 
 | Character Positions | DDRAM Addresses
2  16 2  20 2  24 2  32 2  40 | 00..15 00..19 00..23 00..31 00..39 | 0 00..0 0F + 0 40..0 4F 0 00..0 13 + 0 40..0 53 0 00..0 17 + 0 40..0 57 0 00..0 1F + 0 40..0 5F 0 00..0 27 + 0 40..0 67
DDRAM address usage for a 1-line LCD
DDRAM address usage for a 2-line LCD
Interfacing with LCD cont’d …

## Slide 75
HCS12 MCU
HD44780U-based LCD module
PK5..PK2
DB7..DB4
GND
VEE
VCC
5 V
5 V
RS
E
R/W
PK0
PK1
LCD Interface Example (4-bit bus, used in Dragon12)
Interfacing with LCD cont’d …
Interfacing the HD44780U to Dragon12
It uses 4-bit data transfer. First the upper four bits are sent over DB7 ~ DB4 followed immediately by the lower four bits.
The R/W signal to the LCD kit in the Dragon12 demo board is grounded, which prevents the user from polling the BF flag to determine whether the LCD internal operation has been completed.

## Slide 76
tAS
PWEH
tCYCLE
tAH
tH
tEf
tEr
tDSW
RS
R/W
E
DB0-DB7
Valid data
HD44780U LCD controller write timing diagram
Interfacing with LCD cont’d …
Certain timing parameters must be satisfied in order to access the LCD successfully.
The write timing diagram is shown below and the values of timing parameters are given in a table on next slide.

## Slide 77
Symbol | Meaning | Min. | Typ. | Max. | Unit
tCYCLE PWEH tEr, tEf tAS tDDR tDSW tH tDHR tAH | Enable cycle time Enable pulse width (high level) Enable rise and decay time Address setup time, RS, R/W, E Data delay time Data setup time Data hold time (write) Data hold time (read) Address hold time | 1000 450 -- 60 -- 195 10 5 20 | -- -- -- -- -- -- -- -- -- | -- -- 25 -- 360 -- -- -- -- | ns ns ns ns ns ns ns ns ns
HD44780U LCD bus timing parameters (1 MHz operation)
Interfacing with LCD cont’d …
In the next few slides we will try to develop a set of subroutines that will perform certain functions for the LCD on the Dragon12 demo board such as cmd2lcd, openlcd, putc2lcd,and puts2lcd.

## Slide 78
Interfacing with LCD cont’d …
cmd2lcd:
Write a subroutine that sends the command cmd to the LCD kit.
The procedure for sending a command to the IR register of the LCD is as follows:
    Pull the RS and the E signals to low.
    Pull the R/W signal to low.
    Pull the E signal to high.
    Output data to the output port attached to the LCD data bus. One needs to configure port K for output before writing data to the LCD kit.
    Pull the E signal to low and make sure that the internal operation is complete.
Note that with exception of (clear display & cursor home), every other operation takes 40 s to be completed. For those two commands one needs extra delay loop.

## Slide 79
Interfacing with LCD cont’d …
cmd2lcd PSHA ; save the command in stack
BCLR PORTK,RS ; select the instruction register
BSET PORTK,E ; pull the E signal high
ANDA #$F0 ; clear the lower 4 bits
LSRA ; match the upper four bits
LSRA ; with the LCD data pins
ORAA #E ; Maintain the E signal value
STAA PORTK ; send the command along w/ RS & E
NOP ; extend the duration of E pulse
NOP ;
NOP ;
BCLR PORTK,E ; pull the E signal low
PULA ; retrieve the LCD command
ANDA #$0F ; clear the upper four bits
LSLA ; match the lower four bits
LSLA ; with the LCD data pins
BSET PORTK,E ; pull the E signal high
ORAA #E ; maintain the E signal value
STAA PORTK ; send the lower 4-bit w/RS & E
NOP ; extend the duration of E pulse
NOP ;
NOP ;
450 ns
2 Cycles
1 Cycles
1 Cycles
2 Cycles
2 Cycles
1 Cycles
1 Cycles
1 Cycles

## Slide 80
Interfacing with LCD cont’d …
BCLR PORTK,E ; clear E signal to comp. the operation
* Add 40 s delay to complete the internal operation
LDY #240 ; 240 x 4 = 960 cycles = 40 s
dly DEY ; 1 cycle
BNE dly ; 3 cycles
RTS
RS EQU $01
E EQU $02
Before using the LCD, one must configure it properly. The configuration of the LCD involves at least the following for LCD instructions:
  Entry Mode Set – The common setting for this instruction is to move the cursor to the right after reading or writing a character from/to the LCD.
  Display ON/OFF – The common setting for this instruction is to turn ON the display, cursor, and blinking.

## Slide 81
Interfacing with LCD cont’d …
  Function Set – This instruction sets the number of rows for display, the font size, and the width of the interface data (4 or 8 bits).
  Clear Display – Before outputting any data, it is always a good idea to clear the LCD screen and move the cursor to the home position (upper left corner).
The following subroutine performs the LCD configuration:
openlcd MOVB #$FF,DDRK ; configure port K for output
JSR d_10ms ; wait for LCD to be ready
LDAA #$28 ; set 4-bit data, 2-line display, 58 font
JSR cmd2lcd ;
LDAA #$0F ; turn on display, cursor, and blinking
JSR cmd2lcd ;
LDAA #$06 ; move cursor right (entry mode set
JSR cmd2lcd ; instruction)
LDAA #$01 ; clear the screen and return to home
JSR cmd2lcd ; position

## Slide 82
* Wait until “clear display” command is complete
LDY #10000 ; 10000 x 4 = 40,000 cycles = 1.67ms
dly1 DEY ; 1 cycle
BNE dly1 ; 3 cycles
RTS
d_10ms LDY #60000 ; 60000 x 4 = 240,000 cycles = 10ms
dly DEY ; 1 cycle
BNE dly ; 3 cycles
RTS
Interfacing with LCD cont’d …
The procedure for writing a byte to the LCD data register is as follows:
    Pull the RS signal to high.
    Pull the R/W signal to low.
    Pull the E signal to high.
    Output data to the I/O port attached to the LCD data bus.
    Pull the E signal to low and make sure that the internal operation is complete.

## Slide 83
Interfacing with LCD cont’d …
putc2lcd PSHA ; save the command in stack
BSET PORTK,RS ; select LCD data register
BSET PORTK,E ; pull the E signal high
ANDA #$F0 ; clear the lower 4 bits
LSRA ; match the upper four bits
LSRA ; with the LCD data pins
ORAA #$03 ; keep E & RS signals unchanged
STAA PORTK ; send the upper 4-bit along w/ RS & E
NOP ; extend the duration of E pulse
NOP ;
NOP ;
BCLR PORTK,E ; pull the E signal low
PULA ; retrieve the LCD command
ANDA #$0F ; clear the upper four bits
LSLA ; match the lower four bits
LSLA ; with the LCD data pins
BSET PORTK,E ; pull the E signal high
ORAA #$03 ; keep E & RS signals unchanged
STAA PORTK ; send the lower 4-bit w/RS & E
NOP ; extend the duration of E pulse
NOP ;
NOP ;

## Slide 84
Interfacing with LCD cont’d …
BCLR PORTK,E ; clear E signal to comp. operation
* Add 40 s delay to complete the internal operation
LDY #240 ; 240 x 4 = 960 cycles = 40 s
dly DEY ; 1 cycle
BNE dly ; 3 cycles
RTS
The subroutine that outputs a NULL-terminated string pointed to by the index register X is as follows:
puts2lcd LDAA 1,X+ ; get a character from string
BEQ done_puts ; reach NULL character?
JSR putc2lcd ; if not, output to screen
JMP puts2lcd ; continue till whole string is outputed
done_puts RTS

## Slide 85
Interfacing with LCD cont’d …
#include “C:\Dragon12\examples\Reg9s12.h”
ORG $1000
JSR openlcd ; initialize the LCD
LDX #msg1_lcd ; point to 1st message
JSR puts2lcd ; output it to LCD screen
LDAA #$C0 ; move the cursor to 2nd row
JSR cmd2lcd ;
LDX #msg2_lcd ; point to 2nd message
JSR puts2lcd ;
SWI
msg1_lcd FCC ‘Hello world!’
DC.B 0
msg2_lcd FCC ‘I am ready!’
DC.B 0 ; clear the upper four bits
Write an assembly program to test the previous four subroutines by displaying the following messages on two lines:
Hello world!
I am ready!

## Slide 86
cmd2lcd PSHA ; save the command in stack
BCLR PORTK,RS ; select the instruction register
BSET PORTK,E ; pull the E signal high
ANDA #$F0 ; clear the lower 4 bits
LSRA ; match the upper four bits
LSRA ; with the LCD data pins
ORAA #E ; Maintain the E signal value
STAA PORTK ; send the command along w/ RS & E
NOP ; extend the duration of E pulse
NOP ;
NOP ;
BCLR PORTK,E ; pull the E signal low
PULA ; retrieve the LCD command
ANDA #$0F ; clear the upper four bits
LSLA ; match the lower four bits
LSLA ; with the LCD data pins
BSET PORTK,E ; pull the E signal high
ORAA #E ; maintain the E signal value
STAA PORTK ; send the lower 4-bit w/RS & E
NOP ; extend the duration of E pulse
NOP ;
NOP ;
BCLR PORTK,E ; clear E signal to complete the operation

## Slide 87
* Add 40 ?s delay to complete the internal operation
LDY #240 ; 240 x 4 = 960 cycles = 40 micro_s
sdly DEY ; 1 cycle
BNE sdly ; 3 cycles
RTS
openlcd MOVB #$FF,DDRK ; configure port K for output
JSR d_10ms ; wait for LCD to be ready
LDAA #$28 ; set 4-bit data, 2-line display, 5x8 font
JSR cmd2lcd ;
LDAA #$0F ; turn on display, cursor, and blinking
JSR cmd2lcd ;
LDAA #$06 ; move cursor right (entry mode set
JSR cmd2lcd ; instruction)
LDAA #$01 ; clear the screen and return to home
JSR cmd2lcd ; position
* Wait until “clear display” command is complete
LDY #10000 ; 10000 x 4 = 40,000 cycles = 1.67ms
dly1 DEY ; 1 cycle
BNE dly1 ; 3 cycles
RTS

## Slide 88
d_10ms LDY #60000 ; 60000 x 4 = 240,000 cycles = 10ms
dly DEY ; 1 cycle
BNE dly ; 3 cycles
RTS
putc2lcd PSHA ; save the command in stack
BSET PORTK,RS ; select LCD data register
BSET PORTK,E ; pull the E signal high
ANDA #$F0 ; clear the lower 4 bits
LSRA ; match the upper four bits
LSRA ; with the LCD data pins
ORAA #$03 ; keep E & RS signals unchanged
STAA PORTK ; send the upper 4-bit along w/ RS & E
NOP ; extend the duration of E pulse
NOP ;
NOP ;
BCLR PORTK,E ; pull the E signal low
PULA ; retrieve the LCD command
ANDA #$0F ; clear the upper four bits
LSLA ; match the lower four bits
LSLA ; with the LCD data pins
BSET PORTK,E ; pull the E signal high

## Slide 89
ORAA #$03 ; keep E & RS signals unchanged
STAA PORTK ; send the lower 4-bit w/RS & E
NOP ; extend the duration of E pulse
NOP ;
NOP ;
BCLR PORTK,E ; clear E signal to complete the operation
* Add 40 ?s delay to complete the internal operation
LDY #240 ; 240 x 4 = 960 cycles = 40 ?s
dly2 DEY ; 1 cycle
BNE dly2 ; 3 cycles
RTS
puts2lcd LDAA 1,X+ ; get a character from string
BEQ done_puts ; reach NULL character?
JSR putc2lcd ; if not, output to screen
JMP puts2lcd ; continue till whole string is done
done_puts RTS
getchar EQU $EE84
RS EQU $01
E EQU $02
msg FCC ' ' ; 16 space characters
endmsg DB 0
END

## Slide 90
Create a file with necessary Routines for LCD
‘lcdsubs.asm’
ORG $3000
cmd2lcd
RTS
openlcd
RTS
putc2lcd
RTS
puts2lcd
RTS
d_10ms
RTS
RS EQU $01
E EQU $02

## Slide 91
*****************************************************************************
* Write a program that scrolls LCD display to left-and-right. *
*****************************************************************************
#include reg9s12.h ; include register equates
#include lcdsubs.asm
ORG $1000
JSR openlcd ; initialize the LCD
LDAA #$80 ; start at home position
JSR cmd2lcd
LDAA #$0C ; turn off cursor and blinking
JSR cmd2lcd ;
LDX #msg1
JSR puts2lcd
LDAA #$C0
JSR cmd2lcd
LDX #msg2
JSR puts2lcd
repeat LDAB #4
dloop1 LDAA #$1C ; shift display to the left
JSR cmd2lcd
JSR d_250ms
DBNE B,dloop1
LDAB #4
dloop2 LDAA #$18 ; shift display to the right
JSR cmd2lcd
JSR d_250ms
DBNE B,dloop2
JMP repeat

## Slide 92
d_250ms LDAA #25 ; create 25 ten milisecond delays
DL0 LDY #60000 ;
DL1 DEY ;
BNE DL1 ; scroll buffer by 1
DBNE A,DL0 ;
RTS
msg1 FCC 'Hello There!'
DB 0
msg2 FCC 'I am alive!!'
DB 0
END

## Slide 93
****************************************************************************************
*Write a program that as you type on keyboard it appears on LCD and scrolls *
****************************************************************************************
#include reg9s12.h ; include register equates
#include lcdsubs.asm ; include LCD subroutines
ORG $1000
JSR openlcd ; initialize the LCD
LDAA #$80 ; start at home position
JSR cmd2lcd ;
LDAA #$0C ; turn off cursor and blinking
JSR cmd2lcd ;
nexchar
JMP nexchar ; get next character
Getchar EQU $EE84
msg FCC ' ' ; 16 space characters
endmsg DB 0
END